/** Put this in the src folder **/

#include "i2c-lcd.h"

extern I2C_HandleTypeDef hi2c1;  // change your handler here accordingly

#define SLAVE_ADDRESS_LCD 0x4E // change this according to ur setup

void lcd_send_cmd (char cmd)

{

char data_u, data_l;

uint8_t data_t[4];

//usando il display in 4 bit, devo inviare il comando in due parti (due metà): "u" e "l"

data_u = (cmd&0xf0);

data_l = ((cmd<<4)&0xf0);

data_t[0] = data_u|0x0C;  //en=1, rs=0

data_t[1] = data_u|0x08;  //en=0, rs=0

data_t[2] = data_l|0x0C;  //en=1, rs=0

data_t[3] = data_l|0x08;  //en=0, rs=0

HAL_I2C_Master_Transmit (&hi2c1, SLAVE_ADDRESS_LCD,(uint8_t *) data_t, 4, 100);

}

void lcd_send_data (char data)

{

char data_u, data_l;

uint8_t data_t[4];

//usando il display in 4 bit, devo inviare il comando in due parti (due metà): "u" e "l"

data_u = (data&0xf0);

data_l = ((data<<4)&0xf0);

data_t[0] = data_u|0x0D;  //en=1, rs=1

data_t[1] = data_u|0x09;  //en=0, rs=1

data_t[2] = data_l|0x0D;  //en=1, rs=1

data_t[3] = data_l|0x09;  //en=0, rs=1

HAL_I2C_Master_Transmit (&hi2c1, SLAVE_ADDRESS_LCD,(uint8_t *) data_t, 4, 100);

}

void lcd_clear (void)

{

lcd_send_cmd (0x00);

for (int i=0; i<100; i++)

{

lcd_send_data (' ');

}

}

//THIS ONE

void lcd_put_cur(int row, int col)

{

switch (row)

{

case 0:

col |= 0x00;

break;

case 1:

col |= 0x40;

break;

case 2:

col |= 0x14;

break;

case 3:

col |= 0x54;

break;

}

lcd_send_cmd (col);

}

//or THIS ONE

void lcd16x2_i2c_setCursor(uint8_t row, uint8_t col)

{

uint8_t maskData;

maskData = (col)&0x0F;  //0x0F = 15 decimale

if(row==1)

{

maskData |= (0x80);

lcd_send_cmd(maskData);

}

if(row==2)

{

maskData |= (0x0C);

//maskData = (0x80|0x40);  //non va così

lcd_send_cmd(maskData);

}

if(row==3)

{

maskData |= (0xC0);

lcd_send_cmd(maskData);

}

}

void lcd_init (void)

{

/*Secondo la scheda tecnica (Figura 5 "8-bit interface" del pdf "LCD 20x04 datasheet), per inizializzare l'LCD 20×4

*è necessario inviare qualche sequenza di comandi al display. Cioè i seguenti:*/

// 4 bit initialization

HAL_Delay(50);  // wait for >40ms

//inizializza la modalità 4 bit mandando il comando (0x30) 3 volte con un ritardo di 5ms (?) e il comando (0x20)

lcd_send_cmd (0x30);

HAL_Delay(5);  // wait for >4.1ms

lcd_send_cmd (0x30);

HAL_Delay(1);  // wait for >100us

lcd_send_cmd (0x30);

HAL_Delay(10);

lcd_send_cmd (0x20);  // 4bit mode (?)

HAL_Delay(10);

//display initialization

lcd_send_cmd (0x28); // Function set --> DL=0 (4 bit mode), N = 1 (2 line display) F = 0 (5x8 characters)

HAL_Delay(1);

lcd_send_cmd (0x08); //Display on/off control --> D=0, C=0, B=0  ---> display off

HAL_Delay(1);

lcd_send_cmd (0x01);  // clear display

HAL_Delay(1);

HAL_Delay(1);

lcd_send_cmd (0x06); //Entry mode set --> I/D = 1 (increment cursor) & S = 0 (no shift)

HAL_Delay(1);

lcd_send_cmd (0x0C); //Display on/off control --> D = 1, C, B = 0. (Cursor and blink, last two bits)

}

void lcd_send_string (char *str)

{

while (*str) lcd_send_data (*str++);

}