## Slide 1: HMP for IoT – The path to powerful ultra-efficient nodes
Mike Eftimakis
Linley IoT Conference
IoT Product Manager
July 2017

## Slide 2: Agenda
What is HMP?
HMP for IoT
System design considerations

## Slide 3
What is HMP?

## Slide 4: What is HMP?
MCU
CPU
GPU
ISP
Video
Display
Audio
DSP
DDR
Interconnect
A heterogeneous system
using different compute elements
A heterogeneous subsystem
using different processors cores
Notes: Heterogeneous system is a generic word and means different things when used in different contexts.
We use heterogeneous compute to refer a complex system that combines several different compute elements like CPU, GPU, DSP, Image processor, video processor and a display processor.
We also use the word heterogeneous compute to refer to the combination of different processors – for example ARM’s big.LITTLE technology is an example of heterogeneous compute.
In this talk, we are focusing on the heterogeneous compute using combinations of ARM’s Cortex processors.

## Slide 5: Why heterogeneous computing?
“Right-sized processing”
Increase
system
performance
Increase
system
efficiency
Reduce
system
cost
Notes: Increase system performance
Reduce system power consumption
Increase overall system efficiency
Maximize software reuse
Reduce system cost

## Slide 6: Heterogeneous multicore processors
Multicore
Heterogeneous
Homogeneous
Performance asymmetry
Functional asymmetry
Same ISA
Same microarchitecture
Same view of memory
Same ISA
Different microarchitecture
Same view of memory
OS/Software symmetry
Different ISA
Different microarchitecture
Different view of memory
OS/Software asymmetry
Interconnect
Interconnect
Cortex-A + Cortex-M systems
Interconnect
Notes: People have been doing this for years (decades) – mobile  AP + modem

## Slide 7: Architectural differences between Cortex families
Cortex-A
Cortex-R
Cortex-M
Lower power, smaller area
Higher performance
Rich OS/ RTOS
RTOS only
32/64b ARM and Thumb ISA
32b ARM and Thumb ISA
32b Thumb ISA
SW managed interrupts
HW managed interrupt
AMBA AXI
AMBA AHB/AXI
AMBA AXI
Deterministic SW managed
Operating System
Instruction set
Interrupts
Bus interface
Ideal for user interface and media processing
Ideal for always-on processing
Notes: Many will know difference… but for those who don’t this lists just some of the differences
At a simple level A = higher perf, M = lower power/area and R is in the middle
But there are other feature differences which define each profile
Now some of these are blurring
The cores do overlap in PPA
And features which were previously exclusively in one profile are now starting to appear outside this – so RichOS in Cortex-R
But some things we won’t be doing
-eg ASIL D Cortex-A
-eg adding an MMU to Cortex-M
From a markets point of view you can make some generalisations – A-profile in servers, r-profile in beaking systems, m-profile in microcontrollers
But this picture is also more complicated <click>

## Slide 8
HMP for IoT

## Slide 9: Focus on IoT Nodes and Gateways
Server
Base Station
Global
Applications
Management
Local
Gateway
Sensor
Actuator
IoT Nodes
Small data
Big data

## Slide 10: Characteristics of IoT devices
Power constrained
  Battery operation
  Long usage life
Increasing performance
  More sensors
  Machine learning
  Complex control
Security
Low cost
Always ready
  Most of the time scanning
Side applications
  Voice control
  Smart sensing
Security
Low cost

## Slide 11: Why HMP for IoT?
Need to process locally
  Low power
  High efficiency
  But low-cost
Other reasons
  Reuse SW ecosystem
  Rich UI
  Real-time control
  Context awareness
Cortex-A
Cortex-M

## Slide 12: IoT systems have diverse workloads
Ambient mode
Sensing
Notifications
Time / date
Calendar
Interactive mode
Search
Messages
Audio / Video
Calling
Sleep mode
Regular sampling
Check environment
Wait for trigger
RF scanning
Exception handling
Face recognition
Video streaming
Energy
Energy
Time
Time
Notes: Different requirements – real time vs high performance, general data processing, multimedia

## Slide 13: HMP system example
Chart: Performance
| Cortex-A32 | Cortex-M33
CPU0 | 9.0667 | 1
CPU1 | 9.0667
Chart: Power
| Cortex-A32 | Cortex-M33
Top level | 4.3636 | 1
CPU0 | 29.0909
CPU1 | 29.0909
60x
Less
power
18x
More
performance
Notes: Cortex-A35
  Runs Android OS
  Performance optimized @1.9 GHz
  Quad core cluster with1MB L2 cache
Cortex-M7
  Low power, high performance, always-on sensor hub
  Full config including caches, FPU
  Clock frequency 200 MHz

## Slide 14
System design considerations

## Slide 15: System design considerations
Memory map fusion – partitioning
Security
Power optimization
Inter-processor communication
Software
Debug
Generic HMP compute subsystem using Cortex processors
Interconnect
Shared L2
AHB interconnect
Local memory
DMC
DDR
Cortex-A
subsystem
Cortex-M
subsystem
AHB interconnect
Timer
Sensor
SRAM

## Slide 16: Memory map fusion – subsystem partitioning
Different memory maps
  Cortex-A – 48bit address space
  Cortex-M – 32bit
SMMU to virtualize Cortex-M address space
  Run-time configuration
  Memory mapped dynamically
  Independent application space
Peripherals
  Private – Local
  or shared with access controlled by SMMU
Cortex-A
CPU cluster
Cortex-M
subsystem
AXI interconnect
DMC
AXI /AHB interconnect
AHB interconnect
Timer
Sensor
SRAM
Local memory and peripherals
SMMU
DDR

## Slide 17: Security
Cortex-M and Cortex-A can both support TrustZone
Virtualizing the Cortex-M address space with SMMU
  Each subsystem address space is independent
  Isolation from other Cortex-M systems through the SMMU
  Cortex-A system can control access and sharing
Secure enclave
  Accelerates crypto functions
  Hides keys from the rest of the system
  Form the root of Trust
  Handles life cycle state control and debug access control
Trusted software
Crypto
TRNG
Non-trusted
(normal)
Trusted
(secure)
Trusted hardware
Secure system
Secure
storage

## Slide 18: Power optimization
Multiple power domains
  Reduce leakage current when not in use
Multiple system power state
  Include hibernation when system is idle for a long time
Built-in hardware based power control
  Dynamic power control with reduced SW overhead
Dynamic hierarchical clock gating

## Slide 19: Inter-processor communication
Messaging
  Register based interrupt
  Shared memory for large messages
  Registers for small messages
Requirements
  Split power domain
  Clock crossing
  Receiver power down state

## Slide 20: Example software concept
System Platform . .
Secure processes
Linux
U-Boot
TEE
Provisioning
Security Enclave
SMMU
Secure/Non-Secure Peripherals
Cortex-M Application
RTOS
Secure services
Cortex-A Software Components
Cortex-M Software
Components
Cloud Services
MHU
Secure processes
Secure
Data
Cloud client
Linux Applications
Cloud client

## Slide 21: Example Software Concept 2
System Platform . .
Secure processes
Linux
Secure
Services
Linux Applications
Cloud client
Security Enclave
SMMU
Secure/Non-Secure Peripherals
Cortex-M Application
RTOS
Cortex-A Software
Cortex-M
Software
Cloud Services
MHU
Pico-visor
Secure processes
Cortex-M Application
RTOS
Cortex-M
Software
Secure processes
Memory compartments
configured by the pico-visor

## Slide 22: Debug
Merged debug access solution
  Single Debug Access Port
  Access to each processor subsystem can be independently controlled
Cross triggering and shared timestamp between all systems
Support for certificate authentication
  Multiple CoreSight Authentication “zones”
Configurable trace support

## Slide 23
DS-MDK for Cortex-A/Cortex-M hybrid devices
Debug
Analyze
Optimize
OS awareness
Debug Linux/RTOS apps from a single tool

## Slide 24: Conclusion
HMP is needed to enable more powerful IoT systems
Tools are available to start building HMP systems now
Talk to us about HMP