## Slide 1: Cortex-M4 CPU Core

## Slide 2: Overview
Cortex-M4 Processor Core Registers
Memory System and Addressing
Thumb Instruction Set

## Slide 3: Microcontroller vs. Microprocessor
Both have a CPU core to execute instructions
Microcontroller has peripherals for embedded interfacing and control
  Analog
  Non-logic level signals
  Timing
  Clock generators
  Communications
    point to point
    network
  Reliability and safety
  Power Management

## Slide 4: Cortex-M4 Core

## Slide 5: Architectures and Memory Speed
Load/Store Architecture
  Developed to simplify CPU design and improve performance
    Memory wall: CPUs keep getting faster than memory
    Memory accesses slow down CPU, limit compiler optimizations
    Change instruction set to make most instructions independent of memory
  Data processing instructions can access registers only
    Load data into the registers
    Process the data
    Store results back into memory
  More effective when more registers are available
Register/Memory Architecture
  Data processing instructions can access memory or registers
  Memory wall is not very high at lower CPU speeds (e.g. under 50 MHz)

## Slide 6: ARM Cortex-M4 Core Registers

## Slide 7: ARM Cortex-M4 Core Registers (32 bits each)
R0-R12 - General purpose registers for data processing
  R0-R7 (Low registers) many 16-bit instructions only access these registers;
  R8-R12 (High registers) can be used with 32-bit instructions.
SP - Stack pointer (Banked R13)
  Can refer to one of two SPs
    Main Stack Pointer (MSP)
    Process Stack Pointer (PSP)
  Uses MSP initially, and whenever in Handler mode
  In Thread mode, can select either MSP or PSP using CONTROL register.
LR - Link Register (R14)
  Holds return address when called with Branch & Link instruction (B&L)
PC - program counter (R15)

## Slide 8: Operating Modes
Which SP is active depends on operating mode, and SPSEL (CONTROL register bit 1)
  SPSEL == 0: MSP
  SPSEL == 1: PSP
Similarly, the privileged level in Thread mode depends on the nPRIV(bit 0 of CR)
  nPRIV == 0: privileged level: full access to resources
  nPRIV == 1: unprivileged level: limited access to resources
Thread
Mode. MSP or PSP.
Privileged access or Unprivileged access
Handler Mode
MSP
Reset
Starting Exception Processing
Exception Processing
Completed

## Slide 9: ARM Cortex-M4 Special Registers
xPSR - Program Status Registers
  APSR Application PSR
  EPSR Execution PSR
  IPSR Interrupt PSR (read only, cannot be accessed in unprivileged level)
  These three registers can be accessed as one combined register (PSR)
Interrupt/exception mask registers
  PRIMASK
  FAULTMASK
  BASEPRI
CONTROL – Processor’s control

## Slide 10: ARM Cortex-M4 Program Status Register
Program Status Register (PSR) is three views of same register
  Application PSR (APSR)
    Condition code flag bits Negative, Zero, Overflow, Carry, Sticky Saturation, Great-Than or Equal
  Interrupt PSR (IPSR)
    Holds exception number of currently executing ISR
  Execution PSR (EPSR)
    ICI/IT, Interrupt-Continuable Instruction, IF-THEN instruction
    Thumb state, always 1
 | 31 | 30 | 29 | 28 | 27 | 26:25 | 24 | 23:20 | 19:16 | 15:10 | 9 | 8 | 7 | 6 | 5 | 4:0
APSR | N | Z | C | V | Q |  |  |  | GE |  |  |  |  |  |  | 
IPSR |  |  |  |  |  |  |  |  |  |  |  | Exception Number |  |  |  | 
EPSR |  |  |  |  |  | ICI/IT | T |  |  | ICI/IT |  |  |  |  |  | 

## Slide 11: ARM Cortex-M4 Interrupt/exception mask registers
PRIMASK - Exception mask register
  Bit 0: PM Flag
    Set to 1 to prevent activation of all exceptions with configurable priority
  Access using CPS, MSR and MRS instructions
  Use to prevent data race conditions with code needing atomicity
FAULTMASK – HardFault exception mask register
  Similar to PRIMASK but also blocks HardFault exception
  Equivalent to raising the current exception priority level to -1
BASEPRI
  Mask interrupts based on priority level

## Slide 12: ARM Cortex-M4 special registers
CONTROL
  Bti2: FPCA flag
    Floating point context active: not using(0) or need to save floating point registers(1)
    This bit will be set automatically when floating point instruction is executed, and is 0 by default.
  Bit 1: SPSEL flag
    Selects SP when in thread mode: MSP (0) or PSP (1)
    With OS environment,
    Threads use PSP
    OS and exception handlers (ISRs) use MSP
  Bit 0: nPRIV flag
    Defines whether thread mode is privileged (0) or unprivileged (1)
FPSCR (Optional) – floating point status and control registers

## Slide 13: Memory Maps For Cortex-M4 and MCU
4GB address space(32 bits)
Program code accesses (CODE)
Data (SRAM)
Peripheral
Processor’s internal control and debug components

## Slide 14: Endianness
For a multi-byte value, in what order are the bytes stored?
Little-Endian: Start with least-significant byte
Big-Endian: Start with most-significant byte

## Slide 15: ARMv7E-M Endianness
Cortex-M4 support both Little-Endianness and Big-Endianness
Instructions are always little-endian
Loads and stores to Private Peripheral Bus are always little-endian
Data: Depends on implementation, or from reset configuration
  ST processors are little-endian

## Slide 16: ARM, Thumb and Thumb-2 Instructions
ARM instructions optimized for resource-rich high-performance computing systems
  Deeply pipelined processor, high clock rate, wide (e.g. 32-bit) memory bus
Low-end embedded computing systems are different
  Slower clock rates, shallow pipelines
  Different cost factors – e.g. code size matters much more, bit and byte operations critical
Modifications to ARM ISA to fit low-end embedded computing
  1995: Thumb instruction set
    16-bit instructions
    Reduces memory requirements but also performance
  2003: Thumb-2 instruction set
    Adds some 32 bit instructions
    Improves speed with little memory overhead
  CPU decodes instructions based on whether in Thumb state or ARM state - controlled by T bit

## Slide 17: Instruction Set
Cortex-M4 core implements ARMv7E-M Thumb instructions
Only uses Thumb instructions, always in Thumb state
  Most instructions are 16 bits long, some are 32 bits
  Most 16-bit instructions can only access low registers (R0-R7), but some can access high registers (R8-R15)
Thumb state indicated by program counter being odd (LSB = 1)
  Branching to an even address will cause an exception, since switching back to ARM state is not allowed
Conditional execution supported for both 16-bit and 32-bit(B.W) branch
32 bit address space
Half-word aligned instructions
Upward compatible
Refer to ARMv7M Architecture Reference Manual for specific instructions

## Slide 18: Assembler Instruction Format
<operation> <operand1> <operand2> <operand3>
  There may be fewer operands
  First operand is typically destination (<Rd>) (Exception: memory write)
  Other operands are sources (<Rn>, <Rm>)
Examples
  ADDS <Rd>, <Rn>, <Rm>
    Add registers: <Rd> = <Rn> + <Rm>
  AND <Rdn>, <Rm>
    Bitwise and: <Rdn> = <Rdn> & <Rm>
  CMP <Rn>, <Rm>
    Compare: Set condition flags based on result of computing <Rn> - <Rm>

## Slide 19: Where Can the Operands Be Located?
In a general-purpose register R
  Destination: Rd
  Source: Rm, Rn
  Both source and destination: Rdn
  Target: Rt
  Source for shift amount: Rs
An immediate value encoded in instruction word
In a condition code flag
In memory
  Only for load, store, push and pop instructions

## Slide 20: Update Condition Codes in APSR?
“S” suffix indicates the instruction updates APSR
  ADD vs. ADDS
  ADC vs. ADCS
  SUB vs. SUBS
  MOV vs. MOVS
There are some instructions that update the APSR without explicitly adding S to them since their basic functions are to update the APSR
  CMP
  TST

## Slide 21: Instruction Set Summary
Instruction Type | Instructions
Move | MOV
Load/Store | LDR, LDRB, LDRH, LDRSH, LDRSB, LDM, STR, STRB, STRH, STM
Add, Subtract, Multiply | ADD, ADDS, ADCS, ADR, SUB, SUBS, SBCS, RSBS, MULS
Compare | CMP, CMN
Logical | ANDS, EORS, ORRS, BICS, MVNS, TST
Shift and Rotate | LSLS, LSRS, ASRS, RORS
Stack | PUSH, POP
Conditional branch | IT, B, BL, B{cond}, BX, BLX
Extend | SXTH, SXTB, UXTH, UXTB
Reverse | REV, REV16, REVSH
Processor State | SVC, CPSID, CPSIE, BKPT
No Operation | NOP
Hint | SEV, WFE, WFI

## Slide 22: Load/Store Register
ARM is a load/store architecture, so must process data in registers, not memory
LDR: load register from memory (32-bit)
  LDR <Rt>, source address
STR: store register to memory (32-bit)
  STR <Rt>, destination address

## Slide 23: Addressing Memory
Offset Addressing mode: [<Rn>, <offset>] accesses address <Rn>+<offset>
Base Register <Rn>
<offset> is added or subtracted from base register to create effective address
  Can be an immediate constant, e.g. #0x02
  Can be another register, used as index <Rm>
Auto-update(write back): Can write effective address back to base register- with an exclamation mark(!) at the back
Pre-indexing: use effective address to access memory, then update base register with that effective address
Post-indexing: use base register to access memory, then update base register with effective address

## Slide 24: Other Data Sizes
Load and store instructions can also handle double-word(64 bits) half-word (16 bits) byte (8 bits) and even multiple word (n*32 bits)
Store just writes to double-word half-word or byte without considering sign or unsigned.
  STRH, STRB, STRD, STM
Load a byte or half-word or double-word: What do we put in the upper bits?
How do we extend 0x80 into a full word?
  Unsigned? Then 0x80 = 128, so zero-pad to extend to word 0x0000_0080 = 128
  Signed? Then 0x80 = -128, so sign-extend to word 0xFFFF_FF80 = -128
 | Signed | Unsigned
Byte | LDRSB | LDRB
Half-word | LDRSH | LDRH

## Slide 25: Data Size Extension
Can also extend byte or half-word already in a register
  Signed or unsigned (zero-pad)
How do we extend 0x80 into a full word?
  Unsigned? Then 0x80 = 128, so zero-pad to extend to word 0x0000_0080 = 128
  Signed? Then 0x80 = -128, so sign-extend to word 0xFFFF_FF80 = -128
 | Signed | Unsigned
Byte | SXTB | UXTB
Half-word | SXTH | UXTH

## Slide 26: Load/Store Multiple
LDM/LDMIA: load multiple registers starting from [base register], update base register afterwards
  LDM <Rn>!,<registers>
  LDM <Rn>,<registers>
STM/STMIA: store multiple registers starting at [base register], update base register after
  STM <Rn>!, <registers>
LDMIA and STMIA are pseudo-instructions, translated by assembler
Also, there are two counterparts LDMDB and STMDB: decrement before

## Slide 27: Load Literal Value into Register
Assembly instruction: LDR <rd>, =value
  Assembler generates code to load <rd> with value
Assembler selects best approach depending on value
  Load immediate
    MOV instruction provides 8-bit unsigned immediate operand (0-255)
  Load and shift immediate values
    Can use MOV, shift, rotate, sign extend instructions
  Load from literal pool
    1. Place value as a 32-bit literal in the program’s literal pool (table of literal values to be loaded into registers)
    2. Use instruction LDR <rd>, [pc,#offset] where offset indicates position of literal relative to program counter value
Example formats for literal values (depends on compiler and toolchain used)
  Decimal: 3909
  Hexadecimal: 0xa7ee
  Character: ‘A’
  String: “44??”

## Slide 28: Move (Pseudo-)Instructions
Copy data from one register to another without updating condition flags
  MOV <Rd>, <Rm>
Assembler translates pseudo- instructions into equivalent instructions (shifts, rotates)
  Copy data from one register to another and update condition flags
    MOVS <Rd>, <Rm>
  Copy immediate literal value (0-255) into register and update condition flags
    MOVS <Rd>, #<imm8>

## Slide 29: Stack Operations
Push some or all of registers to stack
  PUSH {<registers>}
  Decrements SP by 4 bytes for each register saved
  Pushing LR saves return address
  PUSH {r1, r2, LR}
Pop some or all of registers from stack
  POP {<registers>}
  Increments SP by 4 bytes for each register restored
  If PC is popped, then execution will branch to new PC value after this POP instruction (e.g. return address)
  POP {r5, r6, r7}

## Slide 30: Add Instructions
Add registers, update condition flags
  ADDS <Rd>,<Rn>,<Rm>
Add registers and carry bit, update condition flags
  ADCS <Rdn>,<Rm>
Add registers
  ADD <Rdn>,<Rm>
Add immediate value to register, update condition flags
  ADDS <Rd>,<Rn>,#<imm3>
  ADDS <Rdn>,#<imm8>

## Slide 31: Add Instructions with Stack Pointer
Add SP and immediate value
  ADD <Rd>,SP,#<imm8>
  ADD SP,SP,#<imm7>
Add SP value to register
  ADD <Rdm>, SP, <Rdm>
  ADD SP,<Rm>

## Slide 32: Address to Register Pseudo-Instruction
Generate a PC-relative address in register
  ADR <Rd>,<label>
How is this used?
  ADR always assembles to one instruction. The assembler attempts to produce a single ADD or SUB instruction to load the address. If the address cannot be constructed in a single instruction, an error is generated and the assembly fails.
  Use the ADRL pseudo-instruction to assemble a wider range of effective addresses.

## Slide 33: Subtract
Subtract immediate from register, update condition flags
  SUBS <Rd>,<Rn>,#<imm3>
  SUBS <Rdn>,#<imm8>
Subtract registers, update condition flags
  SUBS <Rd>,<Rn>,<Rm>
Subtract registers with carry, update condition flags
  SBCS <Rdn>,<Rm>
Subtract immediate from SP
  SUB SP,SP,#<imm7>

## Slide 34: Multiply
Multiply source registers, save lower word of result in destination register, update condition flags
  MULS <Rdm>, <Rn>, <Rdm>
  <Rdm> = <Rdm> * <Rn>
Note: upper word of result is truncated

## Slide 35: Logical Operations
Bitwise AND registers, update condition flags
  ANDS <Rdn>,<Rm>
Bitwise OR registers, update condition flags
  ORRS <Rdn>,<Rm>
Bitwise Exclusive OR registers, update condition flags
  EORS <Rdn>,<Rm>
Bitwise AND register and complement of second register, update condition flags
  BICS <Rdn>,<Rm>
Move inverse of register value to destination, update condition flags
  MVNS <Rd>,<Rm>
Update condition flags by ANDing two registers, discarding result
  TST <Rn>, <Rm>

## Slide 36: Compare
Compare - subtracts second value from first, discards result, updates APSR
  CMP <Rn>,#<imm8>
  CMP <Rn>,<Rm>
Compare negative - adds two values, updates APSR, discards result
  CMN <Rn>,<Rm>

## Slide 37: Shift and Rotate
Common features
  All of these instructions update APSR condition flags
  Shift/rotate amount (in number of bits) specified by last operand
Logical shift left - shifts in zeroes on right
  LSLS <Rd>,<Rm>,#<imm5>
  LSLS <Rdn>,<Rm>
Logical shift right - shifts in zeroes on left
  LSRS <Rd>,<Rm>,#<imm5>
  LSRS <Rdn>,<Rm>
Arithmetic shift right - shifts in copies of sign bit on left (to maintain arithmetic sign)
  ASRS <Rd>,<Rm>,#<imm5>
Rotate right
  RORS <Rdn>,<Rm>

## Slide 38: Reversing Bytes
REV - reverse all bytes in word
  REV <Rd>,<Rm>
REV16 - reverse bytes in both half-words
  REV16 <Rd>,<Rm>
REVSH - reverse bytes in low half-word (signed) and sign-extend
  REVSH <Rd>,<Rm>
MSB
LSB
MSB
LSB
MSB
LSB
MSB
LSB
MSB
LSB
MSB
LSB
Sign extend

## Slide 39: Changing Program Flow - Branches
Unconditional Branches
  B <label>
  Target address must be within 2 KB of branch instruction (-2048 B to +2046 B)
Conditional Branches
  B<cond> <label>
  <cond> is condition - see next page
  B<cond> target address must be within 256 B of branch instruction (-256 B to +256 B)
  Alternatively, can use the B.W as 32-bit version of branch instruction for wider range.

## Slide 40: Condition Codes
Append to branch instruction (B) to make a conditional branch
Full ARM instructions (not Thumb or Thumb-2) support conditional execution of arbitrary instructions
Note: Carry bit = not-borrow for compares and subtractions

## Slide 41: Changing Program Flow - Subroutines
Call
  BL <label> - branch with link
    Call subroutine at <label>
      PC-relative, range limited to PC+/-16MB
    Save return address in LR
  BLX <Rd> - branch with link and exchange
    Call subroutine at address in register Rd
      Supports full 4GB address range
    Save return address in LR
Return
  BX <Rd> branch and exchange
    Branch to address specified by <Rd>
    Supports full 4 GB address space
    BX LR - Return from subroutine

## Slide 42: Special Register Instructions
Move to Register from Special Register
  MSR <Rd>, <spec_reg>
Move to Special Register from Register
  MRS <spec_reg>, <Rd>
Change Processor State - Modify PRIMASK register
  CPSIE - Interrupt enable
  CPSID - Interrupt disable

## Slide 43: Other
No Operation - does nothing!
  NOP
Breakpoint - causes hard fault or debug halt - used to implement software breakpoints
  BKPT #<imm8>
Wait for interrupt - Pause program, enter low-power state until a WFI wake-up event occurs (e.g. an interrupt)
  WFI
Supervisor call generates SVC exception (#11), same as software interrupt
  SVC #<imm>