## Slide 1: Introduction to ARM-based System-on-Chip Design

## Slide 2: Module Syllabus
What is a System-on-Chip
Advantages of SoC
Limitations of SoC
SoC Vs. Microcontroller Vs. Microprocessor
Commercialized SoCs
SoC Examples
SoC Design Flow
What is inside of a SoC
ARM-based SoC
Design a Simple ARM-based SoC
Coming next…
Useful Resources

## Slide 3: What is a System-on-Chip
A System-on-Chip (SoC) is a integrated circuit that packages basic computing components into a single chip.
A SoC has most of the components to power a computer.
Picture source: http://thecustomizewindows.com/, http://www.adafruit.com/
Mother board of a PC
System on a Chip
ARM cores
AMBA buses
Physical IPs

## Slide 4: Advantages of SoC
Higher performance benefiting from:
  Less propagation delay since internal wires are shorter;
  Less gate delay as internal transistors have lower electrical impedance;
Power efficiency benefiting from:
  Lower voltage required (typically < 2.0 volts) compared with external chip voltage (typically >3.0 volts);
  Less capacitance;
Lighter footprint:
  Device size and weight is reduced;
Higher reliability:
  All encapsulated in a single chip package, less interference from the external world;
Low cost:
  The cost per unit is reduced since a single chip design can be fabricated in a large volumes.

## Slide 5: Limitations of SoC
Less flexibility
  Unlike a PC or a laptop, which allows you to upgrade a single component, such as RAM or graphic card, a SoC cannot be easily upgraded after manufacture;
Application Specific
  Most SoCs are specified to particular applications thus they are not easily adapted to other applications.
Complexity
  A SoC design usually requires advanced skills compared with board-level development.

## Slide 6: SoC Vs. Microcontroller Vs. Processor
All implemented on a single chip package, differences include:
Processor (CPU)
  Is a single processor core;
  Normally can be used for general purpose, but needs to be supported with Memories and IOs;
Microcontroller (MCU)
  Typically has a single processor core;
  Has Memory blocks, basic IOs and other basic peripherals;
  Mainly used for basic control purpose, such as embedded applications;

## Slide 7: SoC Vs. Microcontroller Vs. Processor
SoC – System on Chip
  Can have a single or multiple powerful processor cores;
  Has larger Memory blocks, a variety of IOs, and other peripherals;
  Normally integrated with more powerful blocks, e.g. GPU, DSP, video/ audio encoder/ decoder;
  Usually capable of running operating systems, e.g. Windows, Linux, iOS and Android;
  Mainly used for advanced applications, such as the main chip of a digital device (smart phones, tablets).

## Slide 8: Commercialized SoCs
Benefiting from its power efficiency, SoCs have been widely used in mobile devices, such as smartphones, tablets and digital cameras.
A number of SoCs have been developed by a large eco-system of design companies, eg-, SnapdragonTM by Qualcomm®, Tegra® by Nvidia®, Ax by Apple®, OMAPTM by Texas Instruments, etc…
Most mobile SoCs use ARM-based microprocessors since they deliver high performance with less power consumption.

## Slide 9: SoC Example: NVIDIA Tegra 2
Designer | NVIDIA
Year | 2010
Processor | ARM Cortex-A9 (dual-core)
Frequency | Up to 1.2 GHz
Memory | 1 GB 667 MHz LP-DDR2
Graphics | ULP GeForce
Process | 40 nm
Package | 12 x12 mm (Package on Package)
Used in tablets | Acer Iconia Tab A500 Asus Eee Pad Transformer Motorola Xoom Motorola Xoom Family Edition Samsung Galaxy Tab 10.1 Toshiba Thrive
Picture source: http://www.anandtech.com/, http://www.nvidia.com/

## Slide 10: SoC Example: Apple SoC Families
Source:http://en.wikipedia.org/wiki/Apple_(system_on_chip), as of 10/2013
SoC | Model No. | CPU | CPU ISA | Technology | Die size | Date | Devices
N/A | APL0098 | ARM11 | ARMv6 | 90 nm | N/A | 6/2007 | iPhone iPod Touch (1st gen.)
A4 | APL0398 | ARM Cortex-A8 | ARMv7 | 45 nm | 53.29 mm2 | 3/2010 | iPad, iPhone 4, Apple TV (2nd gen.)
A5 | APL0498 | ARM Cortex-A9 | ARMv7 | 45 nm | 122.6 mm2 | 3/2011 | iPad 2, iPhone 4S
 | APL2498 | ARM Cortex-A9 | ARMv7 | 32 nm | 71.1 mm2 | 3/2012 | Apple TV (3rd gen.)
 | APL7498 | ARM Cortex-A9 | ARMv7 | 32 nm | 37.8 mm2 | 3/2013 | AppleTV 3
A5X | APL5498 | ARM Cortex-A9 | ARMv7 | 45 nm | 162.94 mm2 | 3/2012 | iPad (3rd gen.)
A6 | APL0598 | Swift | ARMv7s | 32 nm | 96.71 mm2 | 9/2012 | iPhone 5
A6X | APL5598 | Swift | ARMv7s | 32 nm | 123 mm2 | 10/2012 | iPad (4th gen)
A7 (64-bit) | APL0698 | Cyclone | ARMv8-A | 28 nm | 102 mm2 | 9/2013 | iPhone 5S, iPad mini (2nd gen)
 | APL5698 | Cyclone | ARMv8-A | 28 nm | 102 mm2 | 10/2013 | iPad Air

## Slide 11: SoC Design Flow
Hardware
IP cores
SoC
Design specifics
HW/SW partitioning
Purchase HW cores
Purchase SW drivers
Integrated
Hardware
Integrated
Software
Prototype on platforms
e.g. FPGA
Functional
Simulation
Software
Simulation
Physical optimization
and fabrication
Application development
and test
HW/ SW
co-verification
Volume manufacture
and ship
Software
drivers
IP Vendors:
core design
Fabless Vendors: SoC design
Foundries:
Chip fabrication
PCB manufacture
and device assembly
Device vendors:
Final products

## Slide 12: What is inside of a SoC
The basic components of a SoC include:
  A system master, such as a microprocessor or DSP;
  System peripherals, such as Memory block, timer, external digital/ analog interfaces;
  A system bus that connects master and peripherals together using a specific bus protocol.
More sophisticated modules are integrated in modern SoCs, such as multicores, DSPs, GPUs, and multiple buses connected by bus bridges.
System Master
(Processor)
Data
Memory
Timer
DAC
GPIO
Program
Memory
Watch dog
System Bus
A simple system on Chip

## Slide 13: ARM-based SoC
An basic ARM-based SoC usually consists of
  An ARM processor, such as Cortex-M0;
  Advanced Microcontroller Bus Architecture (AMBA), e.g. AMBA3 or AMBA4;
  Physical IPs (or peripherals) from ARM or third parties;
  Additionally, some SoCs may have a more advanced architecture, such as multi-bus system with bus bridge, DMA engine, clock and power management, etc…
System
Control
ROM
Boot
ROM
RAM
ROM
Table
AHB
Peripheral
APB
Peripheral
UART
Timers
Watch
dog
APB Bus
DMA
Mux
Low latency
AHB IOP
ARM AMBA 3 AHB-Lite System Bus
AHB to APB
Bus bridge
Clock
Generator
Power
Management Unit
JTAG/ Serial wire
RAM
UART
VGA
GPIO
Timer
7-segment
Display
ARM Cortex-M0
Microprocessor
ARM AMBA 3 AHB-Lite System Bus
An example of ARM-based SoC

## Slide 14: Design a Simple ARM-based SoC
In this set of teaching materials we are going to design a simplified version of ARM-based SoC and prototype it onto a FPGA chip. The SoC will consist only some basic components:
  An ARM Cortex-M0 microprocessor;
  A single AHB Lite bus;
  Customer-made physical IPs;
System
Control
ROM
Boot
ROM
RAM
ROM
Table
AHB
Peripheral
ARM AMBA 3 AHB-Lite System Bus
RAM
UART
VGA
GPIO
Timer
7-segment
Display
ARM Cortex-M0
Microprocessor
ARM AMBA 3 AHB-Lite System Bus
EDK: A simplified ARM-based SoC

## Slide 15: Coming next…
In the following modules, you will be:
  Learning ARM Cortex-M0 processor architecture and AMBA3 AHB bus protocol;
  Implementing a basic ARM-based SoC using CortexM0 and AHB bus and prototype them onto a FPGA chip;
  Developing your own hardware peripherals;
  Developing Software drivers for your physical IPs;
  Demonstrating your SoC through a game application (the SNAKE game as shown in the right-side picture).

## Slide 16: Coming next…
You will be following a design flow from low-level hardware implementation to high-level software application design.
SRAM
controller
VGA
Peripheral
UART
Peripheral
Timer
Peripheral
GPIO
Peripheral
7-segment
Peripheral
ARM CMSIS-Core
Application Programming Interface (API)
Application Design (e.g. Game)
ARM Cortex-M0
Processor
Hardware design
Software low-level drivers & libraries programing
Software high-level application development
Peripheral drivers
AHB

## Slide 17: Useful Resources
Reference1
  Book 1: “The Definitive Guide to the ARM Cortex-M0” by Joseph Yiu, ISBN-10: 0123854776, ISBN-13: 978-0123854773, March 11, 2011
Reference2
  Book 2: “ARM System-on-chip Architecture” by Prof Steve Furber, ISBN-10: 0201675196, ISBN-13: 978-0201675191, 17 Aug 2000