## Slide 1: Finite Impulse Response (FIR) Filters

## Slide 2: Moving Average Filter
moving
average
filter
x(n)
y(n)
input
output
five point moving average filter
Notes: The moving average filter is, arguably, the simplest discrete-time (digital) filter of all.
Here is a block diagram representation intended to emphasise that the filter is a (linear time invariant) system and that its input and output are discrete-time signals (or sequences) x(n) an y(n).
For the purposes of illustration we will consider a five point moving average filter.
The nth value of the output signal y(n) is formed by taking the arithmetic mean, or average, of the five most recent values of the input signal x(n).
Here are two slightly different ways of expressing this. The second highlights that the nth value of the output signal is a weighted sum of previous values of the input signal.
Finally, here is a generic expression for an N-point moving average filter.

## Slide 3: Moving Average Filter
input x(n) x
output y(n) ●
Notes: So what does the moving average do to an input signal.
Here’s an example.
The graph shows the discrete values of hypothetical input signal. (blue crosses). Without quantitatively analysing this signal we can observe that over time (as sample number increases) the value of the signal steadily and slowly decreases. This represents a low frequency component in the signal.
From one sample to the next, the value of the input signal jumps up and down. This represents a high frequency component in the signal.
Now let’s apply a five point moving average filter to this signal.
First of all, using the expression on the previous slide, and the information provided here, we cannot ‘properly’ compute values of the output signal y(n) until the sampling instant at which n=4. That value of the output signal will be equal to the arithmetic mean of the first five input signal sample values (the first five blue crosses) on the figure.

## Slide 4: Moving Average Filter
input x(n) x
output y(n) ●
Notes: The next value of the output signal y(5) will be equal to the arithmetic mean of input signal sample values x(1), x(2), x(3), x(4) and x(5), as shown in the next slide.

## Slide 5: Moving Average Filter
input x(n) x
output y(n) ●
Notes: And so on ...

## Slide 6: Moving Average Filter
input x(n) x
output y(n) ●
Notes: And so on ...

## Slide 7: Moving Average Filter
input x(n) x
output y(n) ●
Notes: Without analysing it quantitatively, we can observe that as time progresses the value of the output signal (red blobs) gradually decreases, corresponding to a low frequency component in the output signal.
The value of the output signal from one sample to the next does not ‘jump about’. Compared to the input signal, the output signal is ‘smooth’, and does not contain a high frequency component.
In these terms, the moving average filter has acted as a low pass filter.

## Slide 8: Moving Average Filter
Moving average filter smooths input signal
Filters out or blocks high frequency signal components
Allows low frequency signal components to pass
It is a low pass filter
Notes: To summarise...

## Slide 9: Finite Impulse Response (FIR) Filter
N point moving average filter
Compare this with the conventional representation of an N point FIR filter
h(i) are referred to as the coefficients of the filter
and as the impulse response of the FIR filter
Notes: The moving average filter is one example of a finite impulse response filter. We’ve seen the first expression on this slide before. It describes an N-point moving average filter
Conventionally, the coefficients, or weights, of a finite impulse response filter are given the symbol h.
Each output sample value in a finite impulse response filter is computed from a number of previous input values.
FIR filters are non-recursive.

## Slide 10: FIR filter coefficients
The coefficients, h(i), of an N point moving average
filter each have a value of 1/N
Graphical representation of the coefficients of a 5 point
moving average filter, also known as its impulse response
Notes: Here the coefficients of the five point moving average filter are plotted graphically.
The coefficients may also be referred to as the impulse response of the filter.
For i<0 and i>4, the impulse response is assumed to be zero.
Hence the impulse response is a finite impulse response.

## Slide 11: FIR filter block diagram
Notes: Here is a block diagram representation of the five point moving average filter.
Its component parts are a delay line in which input sample values are stored.
At each sampling instant, the contents of the delay line are shifted by one position and a new input sample value is added.
The coefficients of the filter appear as the gains of the blocks in the middle of the diagram. The output of a block labelled h(i) is equal to its input x(n-i) multiplied by h(i).
A summing junction combines the outputs of the coefficient blocks to form one output sample value, y(n) per sampling instant.

## Slide 12: FIR filter impulse response
Notes: We have stated previously that the impulse response of an FIR filter is equal to its coefficients.
Let’s look at this in block diagram form, by applying an impulse as an input. All values of x(n) are zero except for x(0).
We are assuming here that the values representing previous input samples, stored in the delay line, are initially all equal to zero.

## Slide 13: FIR filter impulse response
1 0 0 0 0
h(0) 0 0 0 0
y(n) = h(0)
Notes: The filter output is a sum of products. However, since all but one value stored in the delay line is equal to zero, all but one of the product terms is equal to zero.
Initially, the output is equal to the first filter coefficient h(0).

## Slide 14: FIR filter impulse response
0 1 0 0 0
0 h(1) 0 0 0
y(n) = h(1)
Notes: At each sampling instant, the contents of the delay line are shifted one position (to the right in this diagram).
Here, n is equal to 1 and the output of the filter is y(1) = h(1).

## Slide 15: FIR filter impulse response
0 0 1 0 0
0 0 h(2) 0 0
y(n) = h(2)
Notes: And so on ...

## Slide 16: FIR filter impulse response
0 0 0 1 0
0 0 0 h(3) 0
y(n) = h(3)

## Slide 17: FIR filter impulse response
0 0 0 0 1
0 0 0 0 h(4)
y(n) = h(4)
Notes: The output of the FIR filter has been formed by convolving the input sequence x with the filter coefficients h.
Convolution is sometimes (correctly) described in terms of ‘sliding’ one sequence across another, forming sums (or integrals) of products along the way.
In the context of this block diagram, the input sequence x has slid across the delay line from left to right while the filter coefficients h have remained stationary with respect to the delay line.

## Slide 18
Frequency response is the (complex) gain of the filter at different
(individual) frequencies
The FIR filter is described by
If input x(n) comprises samples of a continuous complex exponential
(1)
i.e.
FIR filter frequency response
Notes: We have seen qualitatively that the moving average filter is a low pass filter.
What are the quantitative characteristics of the filter in the frequency domain?

## Slide 19
Where
and we consider
Or
Then, substituting for x(n-i) in (1)
(2)
(3)
Frequency Response of the Moving Average Filter

## Slide 20
Comparing equations (2) and (3) we see that if the input x[n]
represents a complex exponential with frequency ω, phase phi
and amplitude A
then the output
represents that input multiplied by a complex gain
that is a continuous, periodic function of ω .
That gain, H(w) represents the frequency response of the filter.
(2)
(3)
(4)
Frequency Response of the Moving Average Filter

## Slide 21: FIR filter impulse response
Expression for complex frequency response of the filter
Hence, the (continuous) frequency response of an FIR filter is found
by taking the DTFT of its coefficients.
Is similar in form to the discrete time Fourier transform (DTFT)
(4)
Notes: Comparing the expression for the frequency response of the filter with that of the discrete time Fourier transform (DTFT) we can see that these are equivalent, given that for an FIR filter h(i) = 0 for i<0 and for i>(N-1)

## Slide 22
in this case, the filter coefficients are given by
Take the DTFT of h(n)
hence
Example: the frequency response of the five-point moving average filter
FIR filter frequency response
Notes: Balancing the exponents of the terms in the frequency response enables the sum of complex exponentials to be converted (using Euler’s formula) into a real-valued trigonometric expression. This separates the phase and magnitude components of the complex frequency response, although you need to remember that the real-valued trigonometric expression is equal to the magnitude of the frequency response only when it is positive. Where it is negative, an extra 180 degrees of phase shift is implied.

## Slide 23
in this case, the filter coefficients are given by
Take the DTFT of h(n)
hence
Example: the frequency response of the five-point moving average filter
FIR filter frequency response
(5)
Notes: Balancing the exponents of the terms in the frequency response enables the sum of complex exponentials to be converted (using Euler’s formula) into a real-valued trigonometric expression. This makes it relatively simple to envisage, or to plot, the magnitude frequency response.
The complex exponential term corresponds to a linear phase response (in this case -2ω), although you need to remember that the real-valued trigonometric expression is equal to the magnitude of the frequency response only when it is positive. Where it is negative, an extra 180 degrees of phase shift is implied.

## Slide 24
Five point Moving Average Filter
Notes: Here are the (continuous) magnitude and phase components of the frequency response plotted over one period (2 pi radians of normalised frequency).
The trigonometric, real-valued part of the frequency response expression is not equal to the magnitude frequency response since it is negative for values
of normalised frequency between -0.8 pi and -0.4 pi, and between 0.4 pi and 0.8 pi. Correcting for this introduces phase shifts of pi/2 (in those frequency
ranges) to the linear phase response of -2ω corresponding to the complex exponential term in equation (). (It’s more straightforward than it looks!)

## Slide 25: Window method of FIR filter design
If we know the coefficients of an FIR filter we can compute its
frequency response.
How do we find the FIR filter coefficients that will give a desired
frequency response?
How do we design an FIR filter?
Notes: These days FIR filters may be designed using any one of a multitude of computer-based filter design packages. As we will consider later, FIR filters may be designed to have arbitrary frequency responses (with constraints). However, it is useful to understand the principles involved in FIR filter design based on widely-used ideal filter prototypes. Underlying all of this is the relationship between finite, discrete-time sequences (signals) and their corresponding periodic, continuous frequency representations, i.e. the discrete time Fourier transform.

## Slide 26: Ideal filter prototypes
Low pass
High pass
Notes: One starting point for the design of an FIR filter is a desired frequency response in one of these ideal forms.

## Slide 27: Ideal filter prototypes
Band pass
Band stop

## Slide 28: Window method of FIR filter design
Design steps
Specify desired frequency response.
Use inverse Fourier transformation to obtain corresponding (discrete) impulse response.
Multiply impulse response (the FIR filter coefficients) by finite tapered window function.
Notes: The window method of FIR filter design takes a desired frequency response as its starting point, (inverse) transforms that into the (discrete) time domain and, for reasons we will see presently, applies a window function to the resulting impulse response (filter coefficients).

## Slide 29: Widely-used window functions
Window functions
Notes: Window functions are, in general, real-valued, symmetrical and tapered. Defined as discrete sets of points as in this slide, the number of points in a window should equal the number of FIR filter coefficients. In a computer program it is likely that window functions and filter coefficients will be indexed from zero through N-1. Alternatively, as in this slide, the indexing may run from –L through L. Type 1 FIR filters having an odd number of coefficients and h(n) are the most useful and are considered in these slides. An FIR filter having N coefficients has order (N-1) and in the notation used in this slide, L = (N-1)/2. Hence the order of the filter is equal to 2L.

## Slide 30: Example of window function
33-point Hanning window

## Slide 31: Low pass FIR filter
Taking inverse DTFT
Order of filter:
Number of coefficients:
for
in the range
Notes: Here is an algebraic expression for an ideal low pass filter. It is straightforward to derive the inverse DTFT of this. h(n) may be evaluated for any value of n from minus to plus infinity. Here we truncate it. Only N=(2L+1) values will be used as filter coefficients.

## Slide 32: Design of a low pass FIR filter
The inverse DTFT of a continuous, ideal (rectangular), low pass frequency response is a discrete-time impulse response (filter coefficients) of infinite extent.
Notes: The inverse DTFT transforms a continuous periodic function of frequency into a discrete aperiodic function of time.
As seen earlier, the DTFT and inverse DTFT are the form of Fourier analysis appropriate for describing the characteristics of an FIR filter.
By its nature, an FIR filter is described by a finite (and hence aperiodic) set of discrete coefficients, and has a continuous frequency response (it has a gain across a continuum of frequencies). In theory its frequency response is periodic (with period 2π measured in normalised frequency or fs measured in actual frequency). In practice, a digital implementation of a filter will have a bandwidth limited to +/- fs/2 and this theoretically implied periodicity will not be observed.

## Slide 33: Design of a low pass FIR filter
A finite impulse response filter has a finite set of coefficients.
Truncating the impulse response corresponding to an ideal low pass frequency response has the effect of introducing ripple.
Truncated, or rectangular-windowed
finite impulse response
Notes: If the infinite set of filter coefficients calculated using the inverse DTFT is truncated to a finite set (symmetrically about n=0), this has implications for the magnitude frequency response of the filter as illustrated here. Compared to the ideal low pass filter, the gain of this filter varies (ripples) as the frequency of the input (and output) signal varies.
If the window is widened, i.e. more filter coefficients are used then the sharpness of the transition from pass band to stop band will increase. (in the case of truncation by a rectangular window, the magnitude of the gain variations in the frequency response will remain the same as before but the ‘ripples’ will be bunched closer to the transition region, cf Gibbs phenomenon.

## Slide 34: Design of a low pass FIR filter
Symmetrical, tapered-windowed
finite impulse response
Multiplying the filter coefficients by a symmetrical, tapered window function reduces ripple at the expense of widening the transition from pass band to stop band.
Notes: If the truncation is effected using a tapered, symmetrical window function rather than the rectangular window implied by straightforward truncation, the gain variations (ripples) in the magnitude frequency response are diminished, at the expense of a rather more gradual transition from pass band to stop band than in the ideal low pass filter.
I like to refer to ‘gain variations’ (as a function of frequency, not time, of course) rather than ripples because I have observed a tendency in students to infer that ‘ripples’ in a frequency response will somehow cause spurious oscillations in the output from a filter. However, on reflection, misunderstanding is possible however you phrase things.

## Slide 35: Design of a low pass FIR filter
The effect of windowing the filter coefficients on the frequency response of a filter is clearer if magnitude is plotted on a log scale.
Notes: This graph shows the two previous (N=33) magnitude frequency responses on a log scale.
Stop band ripple is accentuated.

## Slide 36: High pass FIR filter
Taking inverse DTFT
Order of filter:
Number of coefficients:
for
in the range
Notes: Here is an algebraic expression for the frequency response of an ideal high pass filter. Once again, its inverse DTFT is relatively straightforward to derive.

## Slide 37: Band pass FIR filter
Taking inverse DTFT
Order of filter:
Number of coefficients:
for
in the range
Notes: Here is an algebraic expression for the frequency response of an ideal band pass filter. Once again, its inverse DTFT is relatively straightforward to derive.

## Slide 38: Band stop FIR filter
Taking inverse DTFT
Order of filter:
Number of coefficients:
for
in the range
Notes: Here is an algebraic expression for the frequency response of an ideal band stop filter. Once again, its inverse DTFT is relatively straightforward to derive.

## Slide 39: Window method of FIR filter design
Design steps
Specify desired frequency response.
Use inverse Fourier transformation to obtain corresponding (discrete) impulse response.
Multiply impulse response (the FIR filter coefficients) by finite tapered window function.
Notes: The window method of filter design introduced earlier doesn’t specifically state that the desired frequency response need be specified as a continuous function of frequency, or mention the use of the DTFT.
If the desired frequency response is specified only at discrete frequencies then it may be inverse transformed using the DFT.

## Slide 40: Discrete frequency response
Taking the inverse DTFT of a rectangular function is straightforward
Taking the inverse DTFT (algebraic operation) of a more
sophisticated, or arbitrary, function may be problematic
Alternatively, specify a discrete (desired) frequency response and take its inverse DFT (computational operation).
Notes: One of the advantages of FIR filters (over IIR filters) is that arbitrary frequency response characteristics are possible.
However, it may be problematic to express a desired frequency response algebraically let alone find its inverse DTFT.
An alternative approach, that is consistent with the concept of the window design method is to specify discrete values of a desired frequency response and compute the inverse DFT of those points.
Some of the following points are intuitively obvious but may be worth mentioning.
Discrete points of frequency response are regularly spaced across a normalised frequency range of 2pi radians. N discrete frequency response values will transform into N filter coefficients.
The continuous-time frequency response of the resulting FIR filter (DTFT of the coefficients) will have the specified/anticipated gains at the discrete frequency values used but it is not straightforward to anticipate accurately the gains at intermediate frequencies. In general terms it is likely that the gain variations will appear as ‘ripple’ and this may be reduced by applying a tapered window to the filter coefficients as before, i.e. after they have been computed using the inverse DFT.