## Slide 1: Introduction to IoT

## Slide 2: Syllabus
Introduction to IoT
  What is IoT
  Why and How
  Challenges
Technologies that enable IoT
  Mobile Devices – ARM Cortex-A class processor
  Embedded Devices – ARM Cortex-M class processor
  Networking – BluetoothSmart technology
  Connected Community – ARM mbed platform

## Slide 3: Internet of Things
Internet of Things (IoT)
  IoT is term generally refers to a world in which a large range of objects are addressable via the network
  Objects can include
          Smart buildings and home appliances, e.g. washing machines, TVs, fridges, cookers, doors, chairs…
          Civil engineering structures, e.g. bridges, railways …
          Wearable devices, e.g. smart watches, smart glasses, rings, clothes …
          Medical devices, e.g. embedded pills
          And possibly every THING in the world…

## Slide 4: Internet of Things
Why IoT?
  Items can have more functionalities and become more intelligent
  Items can be managed in an easier way
  More information become available
Why IoT is becoming more realistic?
  Embedded chips are becoming
          Cheaper
          Smaller
          Lower power
      Communication is becoming faster

## Slide 5
Fitness / Healthcare
Portable and Wearable
Electronics
Smart
Lighting
Safer Automotive
Machine to Machine
Smart Appliances
Industrial Internet
Resource
Management
Opportunities......
........and Challenges
Always on
Increased connectivity
Confidentiality
Security
Regulations
New demographic
Smart Farming

## Slide 6: Challenges of Internet of Things
Large amount of chips required
  Chips have to become further cheaper, smaller
Big data demand
  Large volume of data will be generated, data centre storage needs to be increased
Computation requirement
  Requires high performance, such as for cloud computing
Power consumption
  Low power chips, longer battery life, and maybe wireless charging…
Security
  Large amount of private data need to be protected
Standards
  Official standards are required, such as network protocol

## Slide 7: The IoT Opportunity Gap
The IoT Opportunity is much larger
Analysts predictions for connected devices (2020):
30 billion?
50 billion?
75 billion?
Current trend shows strong growth
Not new, it’s been around for >20 years1
Connected things > world population (6.8B)
Reach
Time
Today
Silos of Things
1 Weiser, Mark (1991) “the Computer for the 21st Century”

## Slide 8: IoT Scale and Diversity is Very Different from Mobile
Volume
Device Categories
*Gartner
26 Billion Installed Units by 2020*

## Slide 9: IoT and Home Appliance
The number of Internet-connected devices
projected to be in the home of the average
family of four (with two teenage children) in
2020 — up from an average of about 10
connected devices in 2012.
50
Notes: SOURCE: "Building Blocks for Smart Networks" (Organization for Economic Cooperation and Development, 2013)

## Slide 10: Technologies that enable IoT
Technologies that enable IoT
  Mobile computing – smart, low-power devices, e.g. smartphones, tablet
  Little Devices and Little Data – embedded devices, e.g. wearables, sensors
  Standards that enable internet scale - standardised networking, e.g. wifi, 3G, LTE, Bluetooth Smart, browsers, Javascript, HTTP, TLS etc.
  Web and community based development – eco-system enabled by trust, e.g. mbed, HTML5, etc.

## Slide 11: Technologies that can Enable IoT
Web and community based development
1,000,000s
Platform
Little Devices and Little Data
IEEE 802.15.4
Cortex-M
Devices
Applications
Big Data
Internet of Things
Standards that enable INTERNET scale
LTE
3G
Cortex-A
Mobile Computing

## Slide 12: Technologies that can Enabling IoT
Internet of Things
Cortex-A
Mobile Computing
Notes: Mobile computing
Devices - Smartphones, tablets
Main processor – ARM Cortex-A class processors
OS supports – Android, iOS etc..

## Slide 13: ARM Processors in Smartphones
ARM Cortex-A family:
  Applications processors for feature-rich OS and 3rd party applications
ARM Cortex-R family:
  Embedded processors for real-time signal processing, control applications
ARM Cortex-M family:
  Microcontroller-oriented processors for MCU, ASSP, and SoC applications
Notes: One smartphone is an integration of various ARM-based technologies, ranging from high performance processors, e.g. Cortex-A, to low power oriented processors such as Cortex-M class
ARM Cortex-A family:
  Applications processors for feature-rich OS and 3rd party applications
ARM Cortex-R family:
  Embedded processors for real-time signal processing, control applications
ARM Cortex-M family:
  Microcontroller-oriented processors for MCU, ASSP, and SoC applications

## Slide 14: ARM Cortex-A Class Processors
Used in applications that have high-compute requirements
Run rich operating systems
Deliver interactive media and graphics experience
Notes: Cortex-A17 processor - most efficient mid-range solutions, delivering a new mid-range performance point for any screen - from Mobiles to Smart-TVs
Cortex-A15 processor - highest performance solutions for current mobile and demanding wireless infrastructure applications
Cortex-A12 processor - high performance mid-range solutions targeted at mobile smartphone and tablet devices
Cortex-A9 processor - implementations delivering 800 MHz - 2 GHz typical frequency and delivering 5000 DMIPS of performance per core
Cortex-A7 processor - implementations in standalone, multi-core configurations delivering 800 MHz - 1.2 GHz typical frequency, or in combination with Cortex-A15 processor for big.LITTLE processing
Cortex-A5 processor - in low-cost implementations from 400- 800 MHz delivering over 1200 DMIPS of performance

## Slide 15: ARM Cortex-A Class Processors
Computing
  Smartbook, Tablet, eReader, Thin client
Mobile Handset
  Smartphones, Feature phones
Digital Home
  Set-top Box, Digital TV, Blu-Ray player, Gaming consoles
Automotive
  Infotainment, Navigation
Enterprise
  Laserjet printers, routers, wireless base-stations, VOIP phones and equipment
Wiresless Infrastructure
  Web 2.0, wireless base stations, switches, servers

## Slide 16: ARMv7-A Architecture
ARMv7-A
  The most widely used architecture in mobile devices
  32-bit ARM architecture
  Supports for SMP, VFPv3, NEON, Thumb-2
  Cores include: Cortex-A5, Cortex-A7, Cortex-A8, Cortex-A9, Cortex-A12, Cortex-A15, Cortex-A17

## Slide 17: Technologies that can Enabling IoT
Little Devices and Little Data
Cortex-M
Devices
Applications
Big Data
Internet of Things
Notes: Little devices and little data
Device – sensors, wearables, embedded microcontrollers
Processor - ARM Cortex-M class processors , low-power microcontroller

## Slide 18: Little Data Starts with Little Devices
Little Data
Big Data
Security
Communication
Discovery
Data Storage&Analytics
Management
Applications
Local
processing
Nodes
Nodes
3G
LTE
IEEE 802.15.4
Notes: Requirement of little devices
Connectivity, such as 3G, WiFi, LTE, Bluetooth, Bluetooth Smart, ZigBee…
Low chip cost and small footprint
Low power chips, longer battery life, and maybe wireless charging…
Data security, Large amount of private data need to be protected

## Slide 19: ARM® Cortex® -M - Enabling Little Devices
Omate
Wearable
Memoto
Wearable
Misfit
Wearable
Anki
Toys
IS2T
Embedded Java
Over 250,000 Pebble Watches Sold in 2013
Wearable
Over 2 Billion
ARM® Cortex® -M devices shipped in 2013
by leading semiconductor companies
Silicon Labs EM35x
ZigBee system-on-chip
ARM Cortex-M3 Processor
Dialog Semiconductor DA14580 Bluetooth LE
ARM Cortex-M0 Processor
Freescale KW01 / KW20
Sub-1 GHz / Zigbee
ARM Cortex-M0+/M4 Processor
GainSpan GS2000
WiFi & ZigBee IP (6LoWPAN)
2x ARM Cortex-M3 Processors
Linear LTC5800-IMP
2.4GHz (802.15.4 / 6LoWPAN)
ARM Cortex-M3 Processor
Sierra Wireless AirPrime WP6
2G EDGE system-on-chip
ARM Cortex-M0 Processor
Nordic Semi nRF51822
Bluetooth LE
ARM Cortex-M0 Processor
TI EM35x CC2538
ZigBee system-on-chip
ARM Cortex-M3 Processor
Broadcom BCM20736
Bluetooth LE + wireless charging
ARM Cortex-M3 Processor
Not to be republished without permission from ARM
Notes: Cortex-M series: Cortex-M0, M0+, M1, M3, M4.
Energy-efficiency
  Lower energy cost, longer battery life
Smaller code
  Lower silicon costs
Ease of use
  Faster software development and reuse
Embedded applications
  Smart metering, human interface devices, automotive and industrial control systems, white goods, consumer products and medical instrumentation

## Slide 20: Technologies that can Enabling IoT
IEEE 802.15.4
Internet of Things
Standards that enable INTERNET scale
LTE
3G

## Slide 21: Bluetooth Smart Connectivity
Also known as Bluetooth Low Energy
Ultra low power, designed to run from coin cells, e.g. 10mW
Short range communication, e.g. <100 meters
Enabling IoT small devices
Notes: Ultra Low Power
Small packets
Short RX and TX windows
Coin-cell battery 1+ year
Low memory footprint
Fast connections
Simple stateless operation

## Slide 22: Technologies that can Enabling IoT
Web and community based development
1,000,000s
Platform
Internet of Things
Notes:   mbed is a platform used for easy prototyping and development of applications and systems based on ARM Cortex-M-based microcontrollers
mbed platform provides
  Open software libraries
  Open hardware designs
  Open online tools for professional rapid prototyping of products based on ARM-based microcontrollers

## Slide 23: ARM® mbed™ - Accelerating IoT Deployment
Rapid, professional IoT device development
  An open source platform and libraries for Cortex® -M microcontrollers
Mix & match essential components for your product design
  Microcontrollers, Radios, Sensors, Software stacks
  Bluetooth®, 802.15.4/6LoWPAN, WiFi, Cellular
Simplify integration with cloud services
  Integrated with Sensinode NanoService products
  Embedded agents and APIs for cloud services
MCUs
radios
sensors
Notes: mbed platform includes
  A standards-based C/C++ Software Development Kit (SDK)
  A microcontroller Hardware Development Kit (HDK) and supported development boards
  Integrated Development Environment (IDE), including an online compiler and online developer collaboration tools

## Slide 24: Enabling Industry Scale on ARM
1,000,000+
mbed.org unique visitors in 2012
100,000+
mbed-enabled development
boards shipped
100+
Major OEMs from
diverse industries
are using mbed

## Slide 25: Coming Next…
Segments | Modules
Embedded Computing | ARM based embedded systems
 | ARM Cortex-M processor Architecture
 | Interrupt and Power Consumption
Mobile Computing | ARMv7 Architecture
 | ARM Cortex-A9 processors
 | Smartphones and Appcessory Programming
Network | Bluetooth Smart Connectivity
 | RF Design Basics
 | nRF51-series SoC Architecture
Community based Development | Embedded programing using mbed
 | High-level Programming using mbed SDK
 | System Integration