## Slide 1: Smartphone Programing

## Slide 2: Syllabus
Introduction to smartphone
Smartphone hardware components
Mobile operating systems
Smartphone programming

## Slide 3: Introduction to smartphone

## Slide 4: Introduction to Smartphone
Early phone
  Basic functions, e.g. make and receive telephone calls
  Basic components, including battery, keyboard, SIM card etc.
A smartphone
  More advanced computing capability
  More connectivity
  More features like touchscreen, running apps, web browsing, Wi-Fi etc.
  Can run operating systems such as Android, iOS, Windows, Palm OS, Symbian

## Slide 5: Introduction to Smartphone
A smartphone’s hardware typically consist of
  Display and touch screen
  Camera
  Battery
  Antenna
  Main PCB
          Application processor chip
          Memory chips
          RF transceivers chip
          Power management chip
          Others such as GPS, SIM, video processing, Bluetooth
Chart: Typical cost breakdown
| Display and touch screen | Memory | Mechanical | Application Processor | RF | Others
Typical cost | 34 | 34 | 23 | 15 | 24 | 35

## Slide 6: Smartphone hardware components

## Slide 7: Smartphone Hardware Components
It’s Not Just the Apps Processor
Bluetooth
SIM
GPS
Power Management
WiFi
Cellular Modem
Memory Chip
Apps Processor
Touchscreen Controller

## Slide 8: ARM at the Heart of your Smartphone
ARM
  Designs IPs, such as processor IPs, physical IPs, System IPs, GPU IPs
  Licenses IPs to silicon partners, such as Qualcomm, Samsung, Apple, NVIDIA
  Also provide software supports to silicon partners and application developers
  Is a business to business company that does not manufacture large number of chips or end products
Silicon partners
  Select a set of IP cores from ARM or other third-party IP vendors
  Integrate IP cores into a single chip design
  Give design to semiconductor foundries for chip fabrication

## Slide 9: ARM at the Heart of your Smartphone
It’s Not Just the Apps Processor
Bluetooth Cortex™-M3 & Cortex-M0
SIM Securcore® SC300™
GPS Cortex-M3 & Cortex-M0
Power Management Cortex-M3 & Cortex-M0
WiFi Cortex-R4 & ARM968™
Cellular Modem Cortex-R4, Cortex-R5 &
Cortex- R7
Memory Controller Cortex-M3
Apps Processor
Cortex-A5 (MPCore), Cortex-A9 (MPCore)
Cortex-A15 (MPCore);
Cortex-M4
ARM Mali™ Graphics
Touchscreen Controller Cortex-M0
PLUS
CoreLink™ System IP
Artisan® Physical IP 65-28nm
Development tools

## Slide 10: Smartphone Hardware Components
Mobile application processor
  Is a System-on-Chip (SoC) that supports running applications in a mobile operating system
  Most of them are based on ARM Cortex-A processors since they deliver high performance with less power consumption, e.g. Cortex-A5, Cortex-A9, Cortex-A15
  Examples include SnapdragonTM by Qualcomm®, Tegra® by Nvidia®, Ax by Apple®, OMAPTM by Texas Instruments, etc…
  Could also be used in other mobile devices, such as smartphones, tablets and digital cameras

## Slide 11: Smartphone Hardware Components
Memory chip
  Used for large data storage
  Managed by a memory controller - a piece of hardware that is mainly used for controlling the data flow going to/ from the memory block
Memory controller
  Facilitate the access to the heterogeneous physical devices, e.g. SRAM, DRAM, FLASH, hard disk etc.
  Supporting a variety of memory access modes, such as burst mode, memory paging, etc…
  Usually implemented on ARM Cortex-M based microcontrollers, e.g. Cortex-M3

## Slide 12: Smartphone Hardware Components
RF chip
  Transmits and receives radio frequency for communications such as WiFi, Bluetooth, FM etc.
  ARM Cortex-R processors are commonly used as they can deliver real-time performance. For example, Cortex-R4, Cortex-R5, Cortex-R7
Power management chip
  Used for managing power requirements of the host system
  Supports features such as voltage scaling/ regulating, DC - DC conversion, battery charging, power-source selecting etc.
  ARM Cortex-M processors are commonly used as they can provide efficient control with low power consumption, e.g. Cortex-M0, Cortex-M3

## Slide 13: Smartphone Hardware Components
GPS receiver
  Receives signals from satellites and use it to position itself, with the assist of navigation applications, such as Google map
  Could be implemented on Cortex-M3, Cortex-M0
SIM (Subscriber Identity Module)
  Stores international mobile subscriber identity (IMSI)
  ARM SecureCore processors are enhanced with security features, providing easy development for smart cards and secure ICs
Bluetooth
  Bluetooth is quite often used in short distance communications at low power consumption
  Most Bluetooth modules can be implemented on ARM Cortex-M0 and Cortex-M3 processors

## Slide 14: Mobile Operating System

## Slide 15: Mobile Operating Systems
Mobile OS
  Can be operated on a smartphone, tablet or other mobile devices
  More mobile features compared with OS on PC
          Support touchscreen
          Support more communications features, e.g. cellular Bluetooth, GPS, near field communication (NFC)
          Others like Speech recognition
        Consists of a high-level user interface and a low-level kernel for managing hardware in real-time
        Most well-known mobile operating systems include Android, iOS, Windows etc.
Notes: Programming mobile - Appcessory programing, should be categorised as another subject. In this material, we only brief some fundamental app programming based on Android OS

## Slide 16: Android Operating System
Developed by Google and Open Handset Alliance
Written in Java (for UI), C (for core) and C++
Based on Linux kernel
Software stack
  Application – home, contacts, phone, browser etc.
  Application framework – activity manager, window manager, notification manager, contact provider etc.
  Libraries – surface manager, media framework, OpenGL, webkit etc.
  Linux kernel – display driver, camera driver, Bluetooth driver, flash memory driver, WiFi driver etc.
Applications
Applications
Framework
Libraries
Linux Kernel

## Slide 17: Smartphone Programing

## Slide 18: Android App Design Flow
Android Software Development Kit
  Provides API libraries and developer tools
  Supports debugging apps for Android
App development workflow
  Setup – install Android SDK and tools, create virtual devices
  App development – create a project with source code, e.g. resource files and manifest files
  App debug and test – test app using debugger and instrumentation framework
  App publish – configure and test code in release mode, publicize, sell and distribute app to users
Environment setup
App development
App Debug and test
App Publish

## Slide 19: Application Fundamentals
Creating an Android app
      Programed in Java
      Compiled using Android SDK tools into an Android package – APK file
      APK file contains all the contents to install the app
Running an Android app
      Dependency of an app
          Android OS is a multi-user based Linux system – each app is an user
          Each app has a unique Linux user ID – files in an app can only be accessed by that user ID
          Each process has its own virtual machine – apps run independently
      Process of an app
          Starts when any of the app’s components need to be executed
          Shuts down when it’s no longer needed or memory is required for other apps

## Slide 20: Application Fundamentals
Principle of least privilege
  Each app has the access to only to the components it needs
  Apps do not have access to other components without permission
Data and service share between apps
  Two apps share a single Linux ID – thus can access to each other
  Device data, such as contacts, location, camera, Bluetooth can be shared with the permission from the user

## Slide 21: Android App Components
There are four components – activities, services, content providers and broadcast receivers
Activities
  Single screen user interface, (UI) e.g. a web browser app can have one activity for one
  Independent from each other, thus one can be called from each other at any instance, e.g. Start dialling from a webpage
  Work together to form cohesive user experience
  For example, in your Email app, you have activities such as inbox, outbox

## Slide 22: Android App Components
Services
  Can be started by an activity
  Does not provide an UI
  Runs in the background
  For example, wireless service, playing a music at background
Content provider
  Provides shared data
  Data can be read or modified by other apps, if allowed
  Example: Contact book
  Can also be used for private data

## Slide 23: Android App Components
Broadcast receivers
  Broadcast – an announcement to all apps (system-wide)
  Broadcast receiver responds to those announcement
  Can be from system, such as low battery, or other apps, e.g. a message is received
  No UI but uses notification bar
  Used for inter-app communication
  Minimised interference between apps
Message app
Game app
(current UI)
Message app
broadcast
Broadcast received and
displayed as a notification

## Slide 24: Android App Components
When App-a needs a component from App-b
  App-a sends a message to the system, the message can be called as an intent
  System permits and activates the component for App-a
  System starts processing App-b
  System initialises the related classes
  Component started
  When it is completed, the result is returned to App-a

## Slide 25: Manifest File
The manifest file
  Declares all the components of an app, e.g. activities, services, broadcast receivers and content providers
  Declares component capabilities
  Declares app requirement, such as
          API Level
          HW/ SW features, e.g. Bluetooth service
          API libraries
  Identify user permissions

## Slide 26: Example of Manifest File
<manifest xmlns:android="http://schemas.android.com/apk/res/android"
…>
<uses-permission android:name="android.permission.BLUETOOTH" />
<uses-sdk
android:minSdkVersion="8"
android:targetSdkVersion="18" />
<application
.....
<activity
android:name="com.example.test1.MainActivity"
...
<intent-filter>
<action android:name="android.intent.action.MAIN" />
</intent-filter>
</activity>
…..
</application>
</manifest>
Declare user permission
Declare requirement
Declare activity
Declare intent