## Slide 1: Introduction to Embedded Systems

## Slide 2: Module Outline
Introduction to Embedded Systems
  CPUs vs. MCUs vs. Embedded Systems
  Examples of Embedded Systems
  Options for Building Embedded Systems
  Features of Embedded Systems
Introduction to Internet of Things (IoT)
  What is IoT?
  Why IoT?
  Challenges of IoT
Building Embedded Systems
  Building Embedded System using MCUs
  Introduction to the mbedTM Platform

## Slide 3: Introduction to Embedded Systems

## Slide 4: Introduction to Embedded Systems
What is an Embedded System?
  Application-specific computer system
  Built into a larger system
  Often with real-time computing constraints
Why add a computer to a larger system?
  Better performance
  More functions and features
  Lower cost e.g. through automation
  More dependability
Embedded Computer
Software
Hardware
Input from
Environment
Output to Environment
User Interface
Link to other Systems
Embedded
System

## Slide 5: CPUs vs. MCUs vs. Embedded Systems
Microprocessor (CPU)
  Defined typically as a single processor core that supports at least instruction fetching, decoding, and executing
  Normally can be used for general purpose computing, but needs to be supported with memories and Input/Outputs(IOs)
Instruction fetcher
Instruction decoder
Register banks
ALU
Memory Interface
To memory
blocks
Microprocessor

## Slide 6: CPUs vs. MCUs vs. Embedded Systems
Microcontroller (MCU)
  Typically has a single processor core
  Has memory blocks, Digital IOs, Analog IOs, and other basic peripherals
  Typically used for basic control purpose, such as embedded applications
Microprocessor
Analog IO
Timer
Other
peripheral
Digital IO
Program
Memory
Data
Memory
System Bus
Microcontroller

## Slide 7: CPUs vs. MCUs vs. Embedded Systems
Embedded System
  Typically implemented using MCUs
  Often integrated into a larger mechanical or electrical system
  Usually has real-time constraints
Embedded
System

## Slide 8: Example Embedded System: Bike Computer
Functions
  Speed and distance measurement
Constraints
  Size
  Cost
  Power and Energy
  Weight
Inputs
  Wheel rotation indicator
  Mode key
Output
  Liquid Crystal Display
Use Low Performance Microcontroller
  8-bit, 10 MIPS
Input:
Wheel rotation
Mode key
Output:
Display speed and distance

## Slide 9: Gasoline Automobile Engine Control Unit
Functions
  Fuel injection
  Air intake setting
  Spark timing
  Exhaust gas circulation
  Electronic throttle control
  Knock control
Constraints
  Reliability in harsh environment
  Cost
  Weight
Many Inputs and Outputs
  Discrete sensors & actuators
  Network interface to rest of car
Use High Performance Microcontroller
  E.g. 32-bit, 3 MB flash memory, 150 - 300 MHz

## Slide 10: Options for Building Embedded Systems
Dedicated Hardware
Software Running on Generic Hardware
Implementation | Design Cost | Unit Cost | Upgrades & Bug Fixes | Size | Weight | Power | System Speed
Discrete Logic | low | mid | hard | large | high | ? | very fast
ASIC | high ($500K/ mask set) | very low | hard | tiny - 1 die | very low | low | extremely fast
Programmable logic – FPGA, PLD | low to mid | mid | easy | small | low | medium to high | very fast
Microprocessor + memory + peripherals | low to mid | mid | easy | small to med. | low to moderate | medium | moderate
Microcontroller (int. memory & peripherals) | low | mid to low | easy | small | low | medium | slow to moderate
Embedded PC | low | high | easy | medium | moderate to high | medium to high | fast

## Slide 11: Benefits of Embedded Systems
Greater performance and efficiency
  Software makes it possible to provide sophisticated control
Lower costs
  Less expensive components can be used
  Manufacturing costs reduced
  Operating costs reduced
  Maintenance costs reduced
More features
  Many not possible or practical with other approaches
Better dependability
  Adaptive system which can compensate for failures
  Better diagnostics to improve repair time

## Slide 12: Functions of Embedded Systems
Closed-loop control system
  Monitor a process, adjust an output to maintain desired set point (temperature, speed, direction, etc.)
Sequencing
  Step through different stages based on environment and system
Signal processing
  Remove noise, select desired signal features
Communications and networking
  Exchange information reliably and quickly

## Slide 13: Attributes of Embedded Systems
Interfacing with larger system and environment
  Analog signals for reading sensors
    Typically use a voltage to represent a physical value
  Power electronics for driving motors, solenoids
  Digital interfaces for communicating with other digital devices
    Simple - switches
    Complex – displays
Concurrent, reactive behaviours
  Must respond to sequences and combinations of events
  Real-time systems have deadlines on responses
  Typically must perform multiple separate activities concurrently

## Slide 14: Attributes of Embedded Systems
Fault handling
  Many systems must operate independently for long periods of time, requiring them to handle likely faults without crashing
  Often fault-handling code is larger and more complex than the normal-case code
Diagnostics
  Help service personnel determine problems quickly

## Slide 15: Constraints of Embedded Systems
Cost
  Competitive markets penalize products which don’t deliver adequate value for the cost
Size and weight limits
  Mobile (aviation, automotive) and portable (e.g. handheld) systems
Power and energy limits
  Battery capacity
  Cooling limits
Environment
  Temperatures may range from -40°C to 125°C, or even more

## Slide 16: Impact of Constraints
Microcontrollers used (rather than microprocessors)
  Include peripherals to interface with other devices, respond efficiently
  On-chip RAM, ROM reduce circuit board complexity and cost
Programming language
  Programmed in the C language rather than the Java language (resulting in smaller and faster code, so less expensive MCU)
  Some performance-critical code may be in assembly language (a lower level language)
Operating system
  Typically no OS, but instead simple scheduler (or even just interrupts + main code (foreground/background system)
  If OS is used, likely to be a lean RTOS

## Slide 17: Introduction to Internet of Things (IoT)

## Slide 18: Internet of Things
Internet of Things (IoT)
  IoT as a term generally refers to a world in which a large range of objects are addressable via the network
  Objects can include
    Smart buildings and home appliances, e.g. washing machines, TVs, fridges, cookers, doors, chairs…
    Civil engineering structures, e.g. bridges, railways …
    Wearable devices, e.g. smart watches, smart glasses, rings, clothes …
    Medical devices, e.g. embedded pills
    And possibly every THING in the world…
IoT

## Slide 19: Internet of Things
Why IoT?
  Items can have more functionalities and become more intelligent
  Items can be managed in an easier way
  More information become available
Why IoT is becoming more realistic?
  Embedded chips are becoming
    Cheaper
    Smaller
    Lower power
  Communication is becoming faster

## Slide 20: Challenges of Internet of Things
Large amount of chips required
  Chips have to become even more cheaper, smaller
Big data demand
  Large volume of data will be generated, data centre storage needs to be increased
Computation requirement
  Requires high performance e.g. for cloud computing
Power consumption
  Low power chips, longer battery life, and maybe wireless charging…
Security
  Large amount of private data need to be protected
Standards
  Official standards are required, such as network protocol

## Slide 21: Building Embedded Systems

## Slide 22: Building Embedded Systems using MCUs
In most embedded systems, MCUs are chosen to be the best solution, since they offer:
  Low development and manufacturing cost
  Easy porting and updating
  Light footprint
  Relatively low power consumption
  Satisfactory performance for low-end products
In the following labs, we will learn how to develop a variety of embedded systems, using an easy-to-start MCU design suite: mbedTM platform
  Open software library tools
  Low cost hardware platforms, e.g. NXP mbed LPC1768 board,
  Bluetooth Smart ARM® Cortex®-M0-based nRF51822-mKIT
  development kit from Nordic Semiconductor
  Online Integrated development environment (IDE)
mbed LPC1768 board

## Slide 23: What is mbed Platform
mbed is a platform used for developing applications based on ARM Cortex-M microprocessors
The mbed platform includes:
  mbed Software Development Kit (SDK), consists of
    C/C++ software libraries, such as peripheral drivers, networking, RTOS and runtime environment
    Software tools, such as build tools, test and debug scripts
  mbed Hardware Development Kit (HDK), consist of
    Recipes to build custom hardware devices, such as interface firmware and schematics that can be used to easily create development boards
    mbed hardware platforms – off-the-shelf development boards, such as mbed NXP LPC1768 board, Bluetooth Smart ARM Cortex-M0-based nRF51822-mKIT development kit from Nordic Semiconductor
    mbed supports an online IDE, which provides a free instant-access web-based toolchain for application development

## Slide 24: Coming Next…
Knowledge of embedded systems
  Hardware mechanisms
    Introducing the mbed platform
    Introducing the ARM Cortex-M3 Architecture
    Use Interrupt for low power design
  Software programming
    Programming basics: assembly, C/C++ programing
    Learn to use software libraries: CMSIS, mbed APIs
Develop your own embedded systems
  Analog IOs: ADC, DAC, PMW
  Serial communication: UART, I2C, SPI
  Advanced serial communication: USB, CAN, Bluetooth LE
  Network: Ethernet, TCP/IP, HTTP
  Real-time operating system
  Prototyping applications for Internet of Things

## Slide 25: Useful Resources
Reference
  mbed official website: mbed.org