## Slide 1: Introduction to the mbed Platform

## Slide 2: Module Outline
mbed Overview
  Introduction to mbed
  mbed Software Development Kit (SDK)
  mbed Hardware Development Kit (HDK)
  mbed Development Tools
  mbed Worldwide Developer Community
Examples of mbed Hardware Platforms
  Freedom KL25Z
  NXP LPC1768 Hardware Platform
  Nordic nRF51822 Hardware Platform
mbed and Internet of Things

## Slide 3: mbed Overview

## Slide 4: Introduction to mbed
What is mbed?
  mbed is a platform used for easy prototyping and development of applications and systems based on ARM Cortex-M-based microcontrollers
mbed platform provides
  Open software libraries
  Open hardware designs
  Open online tools for professional rapid prototyping of products based on ARM-based microcontrollers
mbed platform includes
  A standards-based C/C++ Software Development Kit (SDK)
  A microcontroller Hardware Development Kit (HDK) and supported development boards
  Integrated Development Environment (IDE), including an online compiler and online developer collaboration tools

## Slide 5: mbed Software Development Kit
mbed Software Development Kit (SDK) includes:
  Software libraries
    Official C/C++ software libraries
      Start-up code, peripheral drivers, networking, RTOS and runtime environment
    Community-developed libraries and codes
      Cookbook of hundreds of reusable peripheral and module libraries have been built on top of the SDK, which can be used to build your projects faster
  Software tools, such as build tools, test and debug scripts
Other features
  Licensed under the permissive Apache 2.0 licence – all codes can be used in both commercial and personal projects with confidence
  Compatible with different hardware platforms
  Support for multiple tool chains
  Details on how to use the SDK will be
  introduced in later modules

## Slide 6: mbed Hardware Development Kit
The mbed Hardware Development Kit (HDK) provides
  Recipes to build custom hardware devices
    Microcontroller sub-system design files and firmware
    Specifications of all support components and circuits
  mbed hardware platforms, off-the-shelf development boards, such as
  Freedom KL25Z,
    NXP LPC1768 board,
    Bluetooth LE enabled Nordic nRF51822
    board
Benefit of the HDK
  Quick design short-cut using ready-
  made schematics
  Provide easy-to-use USB and debugging
  support
  Compatible with mbed SDK
An example of how a microcontroller sub-system might be used to build an evaluation board

## Slide 7: Integrated Development Environment
The mbed IDE provides an mbed online compiler and toolchain for rapid application development
  Lightweight tools
    Online web-based IDE – your project can be accessed from anywhere
    No installation needed, only web browser needed
  Free-of-charge
  Convenient code sharing
    Everyone can Import
    codes/libraries from others
    Everyone can export
    codes/libraries to the community
Online mbed IDE

## Slide 8: Examples of mbed Hardware Platforms

## Slide 9: Examples of mbed Hardware Platforms
mbed hardware platforms are already manufactured development boards that are:
  Based on the mbed HDK
  Quickest way to get started with the mbed platform
  Specifically optimised for flexible rapid prototyping
  Available from distributors worldwide, examples are:
Nordic nRF51822

## Slide 10: Examples of mbed Hardware Platforms
The Freedom KL25Z hardware platform is used for rapid prototyping of general microcontroller applications, it includes:
  A Freescale KL25Z MCU, with a 32-bit ARM® Cortex™-M0+ core running at 48MHz
  128KB FLASH, 16KB RAM
A variety of peripheral IOs:
        USB (host/device)
    SPI (2)
    I2C (2)
    UART (3)
    PWM (TPM)
    ADC (16 bit)
    DAC (1 x 12 bit)
    Touch Sensor
    GPIO (66)

## Slide 11: Features of Freedom KL25Z
Freescale KL25Z MCU
  High performance ARM® Cortex™-M0+ Core
  48MHz, 16KB RAM, 128KB FLASH
  USB Host/Device, 2 x SPI, 2 x I2C, 3 x UART, 24 x PWM, 6 x ADC, 66 x GPIO, Touch Sensor
Prototyping form-factor
  Arduino compatible pin-out, 81mm x 53mm
  5V USB or 4.5-9V supply
  Built-in USB drag 'n' drop FLASH programmer
mbed.org Developer Website
  Lightweight Online Compiler
  High level C/C++ SDK
  Cookbook of published libraries and projects
Freedom KL25Z

## Slide 12: Architecture of Freescale KL25Z MCU
Freescale KL25Z MCU
Program Flash 128 KB
SRAM 16 KB
ARM® Cortex™– M0+ Core
Debug interfaces
Interrupt Controller
Micro-Trace Buffer
BME
DMA
Phase-locked loop
Frequency-locked loop
Low/high frequency oscillator
Internal reference clocks
GPIOs with interrupt
TSI
16bit ADC x1
Analog comparator x1
6bit DAC
12bit DAC
Internal watchdog
Internal watchdog
I2C x2
Low Power UART x1
Timers 1x 6ch +
2x 2ch
Low Power timer x1
System
Memories and Memory interfaces
Clocks
Security and integrity
Analog
Communication Interfaces
Timers
Human – Machine Interface (HMI)
SPI x2
UART x2
Periodic interrupt timers
Real-Time clock
USB LS/FS x1
RAM
Program Flash

## Slide 13: Architecture of Freedom KL25Z Board
KL25Z MCU
  A MCU based on ARM Cortex-M0+ microprocessor
Interface microcontroller
  Provide an USB interface to external devices
  When downloading the program, it receives the program file from your computer, and saves it to the FLASH memory on the mbed board
  When programming the KL25Z microcontroller (after reset), it reads the latest program file from the FLASH memory and transfers it to the KL25Z via UART or SWD interface
Flash memory
  Used to store the program file, the latest updated file will be used by the KL25Z after reset
  128KB storage

## Slide 14: Architecture of Freedom KL25Z Board
Power management
  Made up of two voltage regulators
  For standard applications, e.g. requiring 3.3V voltage, the KL25Z can be powered from the USB
  For applications requiring a higher voltage, the KL25Z can be powered from an external 4.5 – 9V input (labelled as Vin)
  Power can also be sourced from the KL25Z (Vu and Vout)

## Slide 15: Architecture of Freedom KL25Z Board
Freedom KL25Z

## Slide 16: Freescale KL25Z MCU
The KL25Z is a Cortex-M0+ microcontroller for embedded applications
  Featuring a high level of integration and low power consumption
  Typically run at 48MHz frequency
  128 KB of flash memory, 16 KB of data memory
  Offers a variety of IO interfaces, such as USB, DMA, UART, SPI, I2C, ADC, DAC, motor control PWM, timers, and general purpose PWM
Proposed applications
  eMetering
  Lighting
  Industrial networking
  Alarm systems
  White goods
  Motor control
Freescale KL25Z MCU

## Slide 17: Freescale KL25Z MCU
SPI serial I/O controller
  Serial Peripheral Interface (SPI) is a serial interface designed to handle multiple masters and slaves connected to a given bus
I2C bus serial I/O controllers
  The I2C-bus is bidirectional for inter-IC control using only two wires: a Serial Clock line (SCL) and a Serial DAta line (SDA)
Pulse width modulator (PWM)
  PWM is a modulation technique which can be used to conform the width of pulses to control the power supply of electrical devices e.g. motors
  PWM is implemented based on a timer and counters

## Slide 18: Freescale KL25Z MCU
UARTs
  Supports for 3x Universal asynchronous receiver/transmitter (UART) interfaces
  Maximum data bit rate of 6.25 Mbit/s
  16 B Receive and Transmit FIFOs
USB interface
  The Universal Serial Bus (USB) controller is available as device/Host/OTG controller
  4-wire bus that supports communication between a host and one or more (up to 127) peripherals
  Enables 12 Mbit/s data exchange with a USB Host controller

## Slide 19: Freescale KL25Z MCU
16-bit ADC
  A single 16-bit successive approximation Analog to Digital Convertor (ADC) with eight channels and DMA support.
12-bit DAC
  The Digital to Analog Convertor (DAC) allows to generate a variable analog output
  The maximum output value of the DAC is reference voltage VREFP
Memory Protection Unit (MPU)
  Can be used to improve the reliability of an embedded system by protecting critical data within the user application
  Separates the memory into distinct regions and implements protection by preventing disallowed accesses

## Slide 20: Freescale KL25Z MCU
Nested Vectored Interrupt Controller (NVIC)
  Allows for low interrupt latency and efficient processing of late arriving interrupts
General purpose Direct Memory Access (DMA) Controller
  DMA – allows certain hardware peripherals to access the memory independently of the processor core
    Without DMA, the processor core is responsible (probably fully occupied) for transferring data between memory and hardware peripherals
    With DMA, the processor core only needs to initiate the transfer and then hands over to DMA; then the DMA will start transferring and the processor core can do other operations while the transfer is in progress
  The GPDMA enables peripheral-to-memory, memory-to-peripheral, peripheral-to-peripheral, and memory-to-memory transactions

## Slide 21: Nordic nRF51822 Hardware Platform
Nordic nRF51822 – an mbed enabled Internet of Things (IoT) starter kit
  The nRF51822-mKIT is a low cost ARM mbed enabled development board for Bluetooth Low Energy (a.k.a Bluetooth LE or Bluetooth Smart) designs with the nRF51822 SoC
  Bluetooth Smart is quickly becoming a key communication component for Internet of Things devices - already supported in modern smartphones and tablets
  Bluetooth Smart is designed for enabling short-range wireless connectivity to things like coin cell-powered accessories
  31 general purpose IO’s accessible on pin header
  mbed-enabled
Nordic nRF51822 Hardware Platform

## Slide 22: Nordic nRF51822 Hardware Platform
Highlights nRF51822:
Combines Bluetooth v4.1-compliant 2.4GHz multiprotocol radio and ARM® Cortex®-M0 processor on a single chip optimized for ultra-low power operation
31 general purpose IOs accessible on pin header; with SPI, I2C, UART
Programmable using mbed tools - USB drag and drop programming
Accepts power through USB, external source, single 2032 coin-cell battery, onboard battery holder
Pin header for current measurement

## Slide 23: mbed and Internet of Things

## Slide 24: mbed and Internet of Things (IoT)
One major role of IoT is to connect the world’s objects in an interoperable standards-based way
To build these standards, mbed provides tools and facilities to rapidly prototype these things to build working proof-of-concepts
Apart from the fast prototyping tools/platforms, mbed also provides special features for IoT development, including:
  Support for HTML5 web standards – a new protocol in HTML version 5 that supports easy real-time data links from any source to any destination
  ARM Sensinode NanoServiceTM – provides end-to-end software products that bring IP and web services to the end node
  mbed world-wide community – a huge open source repository of codes and libraries shared among developers worldwide

## Slide 25: Useful Resources
Freedom KL25Z Schematic
  http://cache.freescale.com/files/soft_dev_tools/hardware_tools/schematics/FRDM-KL25Z_SCH.pdf
Freedom KL25Z Product Brief
  http://cache.freescale.com/files/32bit/doc/prod_brief/KL25PB.pdf?fr=g
Explore the mbed platform
  http://mbed.org/explore/
Freescale KL25Z MCU
  Freedom KL25Z Homepage
    http://www.freescale.com/webapp/sps/site/prod_summary.jsp?code=FRDM-KL25Z
  Freedom KL25Z User Manual
    http://cache.freescale.com/files/32bit/doc/user_guide/FRDMKL25ZUM.zip?fpsp=1&Parent_nodeId=1347555176575735306610&Parent_pageType=product
  Freedom KL25Z Data Sheet
    http://cache.freescale.com/files/32bit/doc/data_sheet/KL25P80M48SF0.pdf