## Slide 1: The ARM Cortex-M0+ Processor Architecture Part-1

## Slide 2: Module Syllabus
ARM Architectures and Processors
  What is ARM Architecture
  ARM Processor Families
  ARM Cortex-M Series
  Cortex-M0+ Processor
  ARM Processor vs. ARM Architectures
ARM Cortex-M0+ Processor
  Cortex-M0+ Processor Overview
  Cortex-M0+ Block Diagram
  Cortex-M0+ Registers

## Slide 3: ARM Architectures and Processors

## Slide 4: What is ARM Architecture
ARM architecture is a family of RISC-based processor architectures
  Well-known for its power efficiency;
  Hence widely used in mobile devices, such as smartphones and tablets
  Designed and licensed to a wide eco-system by ARM
ARM Holdings
  The company designs ARM-based processors;
  Does not manufacture, but licenses designs to semiconductor partners who add their own Intellectual Property (IP) on top of ARM’s IP, fabricate and sell to customers;
  Also offer other IP apart from processors, such as physical IPs, interconnect IPs, graphics cores, and development tools.

## Slide 5: ARM Processor Families
Cortex-A series (Application)
  High performance processors capable of full Operating System (OS) support;
  Applications include smartphones, digital TV, smart books, home gateways etc.
Cortex-R series (Real-time)
  High performance for real-time applications;
  High reliability
  Applications include automotive braking system, powertrains etc.
Cortex-M series (Microcontroller)
  Cost-sensitive solutions for deterministic microcontroller applications;
  Applications include microcontrollers, mixed signal devices, smart sensors, automotive body electronics and airbags;
SecurCore series
  High security applications.
Previous classic processors
  Include ARM7, ARM9, ARM11 families
Cortex-A
Cortex-A57
Cortex-A53
Cortex-A15
Cortex-A9
Cortex-A8
Cortex-A7
Cortex-A5
Cortex-R7
Cortex-R5
Cortex-R4
Cortex-M4
Cortex-M3
Cortex-M1
Cortex-M0+
Cortex-M0
SC000
SC100
SC300
ARM11
ARM9
ARM7
Cortex-R
Cortex-M
SecurCore
Classic
As of Dec 2013

## Slide 6: Design an ARM-based SoC
Select a set of IP cores from ARM and/or other third-party IP vendors
Integrate IP cores into a single chip design
Give design to semiconductor foundries for chip fabrication
ARM-based
SoC
ROM
ARM
processor
RAM
System bus
Peripherals
External Interface
SoC
SoC Design
Chip Manufacture
Licensable IPs
IP libraries
Cortex-A9
Cortex-R5
Cortex-M0+
ARM7
ARM9
ARM11
AXI bus
AHB bus
APB bus
GPIO
I/O blocks
Timer
DRAM ctrl
FLASH ctrl
SRAM ctrl

## Slide 7: ARM Cortex-M Series
Cortex-M series: Cortex-M0, M0+, M1, M3, M4.
Energy-efficiency
  Lower energy cost, longer battery life
Smaller code
  Lower silicon costs
Ease of use
  Faster software development and reuse
Embedded applications
  Smart metering, human interface devices, automotive and industrial control systems, white goods, consumer products and medical instrumentation
As of Dec 2013

## Slide 8: ARM Processors vs. ARM Architectures
ARM architecture
  Describes the details of instruction set, programmer’s model, exception model, and memory map
  Documented in the Architecture Reference Manual
ARM processor
  Developed using one of the ARM architectures
  More implementation details, such as timing information
  Documented in processor’s Technical Reference Manual
ARMv4/v4T Architecture
ARMv5/ v4E Architecture
ARMv6 Architecture
ARMv7
Architecture
ARM v6-M
e.g. Cortex-M0, M1
e.g. ARM7TDMI
e.g. ARM9926EJ-S
e.g. ARM1136
ARMv8 Architecture
ARMv7-A
e.g. Cortex-A9
ARMv7-R
e.g. Cortex-R4
ARMv7-M
e.g. Cortex-M3
ARMv8-A
e.g. Cortex-A53
Cortex-A57
ARMv8-R
As of Dec 2013

## Slide 9: ARM Cortex-M Series Family
Processor | ARM Architecture | Core Architecture | Thumb® | Thumb®-2 | Hardware Multiply | Hardware Divide | Saturated Math | DSP Extensions | Floating Point
Cortex-M0 | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M0+ | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M1 | ARMv6-M | Von Neumann | Most | Subset | 3 or 33 cycle | No | No | No | No
Cortex-M3 | ARMv7-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | No | No
Cortex-M4 | ARMv7E-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | Yes | Optional

## Slide 10: ARM Cortex-M0+ Processor Overview

## Slide 11: Cortex-M0+ Processor Overview
Cortex-M0+ Processor
  Entry-level 32-bit ARM Cortex processor designed for a broad range of embedded applications
  An optimized superset of the Cortex-M0
High Performance Efficiency
  11.21 µW/MHz dynamic power requirement
Low Power Consumption
  Longer battery life – especially critical in mobile products
Enhanced Determinism
  The critical tasks and interrupt routines can be served quickly in a known number of cycles
Lower Cost
  Reduced 32-bit-based system cost, close to those legacy 8-bit and 16-bit devices (e.g. can be priced at less than $1)

## Slide 12: Cortex-M0+ Processor Features
32-bit Reduced Instruction Set Computing (RISC) processor
Von Neumann architecture
Instruction set
  Based on the 16-bit Thumb® instruction set and includes Thumb®-2 technology
  High code density with 32-bit performance
2-stage pipeline
Performance efficiency
  0.95-1.36 DMIPS/MHz (Dhrystone Million Instructions Per Second / MHz)
Supported Interrupts
  Non-maskable Interrupt (NMI) + 1 to 32 physical interrupts
  4 interrupt priority levels

## Slide 13: Cortex-M0+ Processor Features
Supports Sleep Modes
  Integrated WFI and WFE Instructions and Sleep On Exit capability
  Optional Retention Mode with ARM Power Management Kit
  Sleep & Deep Sleep Signals
Enhanced Instructions
  Single-Cycle (32x32) Multiply
Debug
  JTAG or 2-pin Serial-Wire Debug (SWD) Ports
  Up to 4 Breakpoints and up to 2 Watchpoints
Memory Protection Unit (MPU)
  Optional 8 region MPU with sub regions and background region
Trace
  Optional Micro Trace Buffer

## Slide 14: Cortex-M0+ Processor Features
ARM Cortex-M0+ Implementation Data |  |  | 
Process | 180ULL (7-track, typical 1.8v, 25C) | 90LP (7-track, typical 1.2v, 25C) | 40G 9-track, typical 0.9v, 25C)
Dynamic Power | 52 µW/MHz | 9.8 µW/MHz (8.17 µA/MHz) | 3 µW/MHz
Floorplanned Area | 0.13 mm2 | 0.035 mm2 | 0.009 mm2
Cortex-M0+ processor is designed to meet the challenges of low dynamic power constraints while retaining light footprints
  180 nm ultra low power process –52 µW/MHz
  90 nm low power process – 9.8 µW/MHz
  40 nm G process – 3 µW/MHz

## Slide 15: Cortex-M0+ Block Diagram
Breakpoint & Watchpoint Units
Optional Debug
Debugger Interface
Nested Vectored Interrupt Controller (NVIC)
Bus Matrix
Cortex-M0+ processor
core
Optional Memory Protection Unit (MPU)
Cortex-M0+ Processor
Optional Micro Trace Buffer (MTB)
Optional Debug Access Port
Optional Wakeup Interrupt Controller (WIC)
Interrupts
Optional single-cycle I/O port
AHB-Lite interface to system
Optional Serial-Wire or JTAG debug port
Cortex-M0+ Components

## Slide 16: Cortex-M0+ Block Diagram
Processor core
  Contains internal registers, the ALU, data path, and some control logic
  Registers include sixteen 32-bit registers for both general and special usage
Processor pipeline stages
  All loads and stores always complete in program order
  All Strongly-ordered load/stores are automatically synchronized to the instruction stream
  Device and Normal load/stores may be pipelined
  Up to two instructions can be fetched in one transfer (16-bit instructions)
Time
Fetch
Execute
Fetch
Execute
Fetch
Execute
Fetch
Execute
Instruction 1
Instruction 2
Instruction 3
Instruction 4

## Slide 17: Cortex-M0+ Block Diagram
Nested Vectored Interrupt Controller (NVIC)
  Up to 32 external interrupt inputs, each with four levels of priority and a dedicated Non-maskable Interrupt (NMI) input
  Automatically handles nested interrupts, such as comparing priorities between interrupt requests and the current priority level
Wakeup Interrupt Controller (WIC)
  For low-power applications, the microcontroller can enter sleep mode by shutting down most of the components
  When an interrupt request is detected, the WIC can inform the power management unit to power up the system
Memory Protection Unit (optional)
  Used to protect memory content, e.g. make some memory regions read-only or preventing user applications from accessing privileged application data

## Slide 18: Cortex-M0+ Block Diagram
Bus interconnect
  Single 32-bit AMBA-3 AHB-Lite system interface that provides simple integration to all system peripherals and memory
  Optional single 32-bit single-cycle I/O port
  Optional single 32-bit slave port that supports the DAP
Debug subsystem
  Handles debug control, program breakpoints, and data watchpoints
  When a debug event occurs, it can put the processor core in a halted state, where developers can analyse the status of the processor at that point, such as register values and flags
  Support for unlimited software breakpoints using BKPT instruction
  Non-intrusive access to core peripherals and zero-waitstate system slaves through a compact bus matrix. A debugger can access these devices, including memory, even when the processor is running

## Slide 19: ARM Cortex-M0+ Processor Registers

## Slide 20: Cortex-M0+ Registers
Processor registers
  The internal registers are used to store and process temporary data within the processor core
  All registers are inside the processor core, hence they can be accessed quickly
  Load-store architecture
    To process memory data, they have to be first loaded from memory to registers, processed inside the processor core using register data only, and then written back to memory if needed
Cortex-M0+ registers
  Register bank
    Sixteen 32-bit registers (thirteen are used for general-purpose);
  Special registers

## Slide 21: Cortex-M0+ Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status Registers (PSR)
Interrupt mask register
Stack definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General purpose
register

## Slide 22: Cortex-M0+ Registers
R0 – R12: general purpose registers
  Low registers (R0 – R7) can be accessed by any instruction
  High registers (R8 – R12) sometimes cannot be accessed e.g. by some Thumb (16-bit) instructions
R13: Stack Pointer (SP)
  Records the current address of the stack
  Used for saving the context of a program while switching between tasks
  Cortex-M0+ has two SPs: Main SP, used in applications that require privileged access e.g. OS kernel, and exception handlers, and Process SP, used in base-level application code (when not running an exception handler)
R15: Program Counter (PC)
  Records the address of the current instruction code
  Automatically incremented by 4 at each operation (for 32-bit instruction code), except branching operations
  A branching operation, such as function calls, will change the PC to a specific address, meanwhile it saves the current PC to the Link Register (LR)
  On reset processor loads PC with the value of the reset vector, that is at address 0x00000004. Bit[0] of the value is loaded into the EPSR T-bit at reset and must be 1.
Data
Data
PC
SP
Address
Low
High
PUSH
POP
Stack
Code
Heap

## Slide 23: Cortex-M0+ Registers
R14: Link Register (LR)
  The LR is used to store the return address of a subroutine or a function call
  The program counter (PC) will load the value from LR after a function is finished
PC
LR
Main
Program
code
subroutine
Current PC
Load PC with the address in LR to return to the main program
Current LR
Return from a subroutine to the main program
PC
LR
Main
Program
code
subroutine
Current PC
1. Save current
PC to LR
2. Load PC with the starting address of the subroutine
Call a subroutine
Code region
Code region

## Slide 24: Cortex-M0+ Registers
Program Status Register (PSR)
  Provides information about program execution and ALU flags
    Application PSR (APSR) – condition code flag bit Negative, Zero, oVerflow, Carry
    Interrupt PSR (IPSR) – holds exception number of currently executing ISR
    Execution PSR (EPSR) – Thumb state
N
Z
C
V
ISR number
Reserved
Reserved
Reserved
T
Reserved
ISR number
APSR
IPSR
EPSR
PSR
bit0
bit8
bit16
bit24
bit31
T
N
Z
C
V

## Slide 25: Cortex-M0+ Registers
APSR
  N: negative flag – set to one if the result from ALU is negative
  Z: zero flag – set to one if the result from ALU is zero
  C: carry flag – set to one if an unsigned overflow occurs
  V: overflow flag – set to one if a signed overflow occurs
IPSR
  ISR number – current executing interrupt service routine number
EPSR
  T: Thumb state – always one since Cortex-M0+ only supports the Thumb state (more on processor states in the next module)

## Slide 26: Cortex-M0+ Registers
Interrupt mask registers
  Bit 0: PM Flag
        Set to one to prevent activation of all exceptions with configurable priority
  Access using CPS, MSR and MSR instructions
    Use to prevent data race conditions with code needing atomicity
CONTROL: special register
  Bit 1: SPSEL Flag
      Selects SP when in thread mode: MSP (0) or PSP (1)
    Bit 0: nPRIV Flag
      Defines whether thread mode is privileged (0) or unprivileged (1)
    With OS environment,
    Threads use PSP
    OS and exception handlers (ISRs) use MSP

## Slide 27: Cortex-M0+ Registers
Reserved
CONTROL
bit8
bit16
bit24
bit31
Reserved
PRIMASK
PRIMASK
SPSEL
nPRIV

## Slide 28: Useful Resources
Reference 1
  Cortex-M0+ Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0484c/DDI0484C_cortex_m0p_r0p1_trm.pdf
Reference 2
  Cortex-M0+ Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0662b/DUI0662B_cortex_m0p_r0p1_dgug.pdf
Reference 3
  Cortex-M0+ Processor Overview:
  http://www.arm.com/products/processors/cortex-m/cortex-m0plus.php