## Slide 1: The ARM Cortex-M0+ Processor Architecture Part-2

## Slide 2: Module Syllabus
Cortex-M0+ Memory Map
  Cortex-M0+ Memory Map
  Bit-band Operations
  Cortex-M0+ Program Image and Endianness
ARM Cortex-M0+ Processor Instruction Set
  ARM and Thumb Instruction Set
  Cortex-M0+ Instruction Set

## Slide 3: ARM Cortex-M0+ Processor Memory Map

## Slide 4: Cortex-M0+ Memory Map
The Cortex-M0+ processor has 4 GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined as a number of regions
  Each region is given for recommended usage
  Easy for software programmer to port between different devices
Nevertheless, despite of the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus

## Slide 5: Cortex-M0+ Memory Map
Private peripherals
e.g. NVIC, SCS
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH
System
External device
External RAM
Peripheral
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
(PPB)
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
KL25Z128VLK4
0x20002FFF
0x20000000
16 KB SRAM
SRAM_U (3/4)
SRAM_L (1/4)
0x1FFFF000
0x0001FFFF
128 KB Flash
0x00000000

## Slide 6: Cortex-M0+ Memory Map
Code Region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM Region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM or other types
Peripheral Region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals
  On-chip peripherals

## Slide 7: Cortex-M0+ Memory Map
External RAM Region
  Primarily used to store large data blocks, or memory caches
  Off-chip memory, slower than on-chip SRAM region
External Device Region
  Primarily used to map to external devices
  Off-chip devices, such as SD card
Internal Private Peripheral Bus (PPB)
  Used inside the processor core for internal control
  Within PPB, a special range of memory is defined as System Control Space (SCS)
  The Nested Vectored Interrupt Controller (NVIC) is part of SCS

## Slide 8: Cortex-M0+ Memory Map Example
AHB bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M0+
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon

## Slide 9: Bit-band Operations
Bit-band operation allows a single load/store operation to access a single bit in the memory, for example, to change a single bit of one 32-bit data:
  Normal operation without bit-band (read-modify-write)
    Read the value of 32-bit data
    Modify a single bit of the 32-bit value (keep other bits unchanged)
    Write the value back to the address
  Bit-band operation
    Directly write a single bit (0 or 1) to the “bit-band alias address” of the data
Bit-band alias address
  Each bit-band alias address is mapped to a real data address
  When writing to the bit-band alias address, only a single bit of the data will be changed

## Slide 10: Bit-band Operation Example
For example, in order to set bit[3] in word data in address 0x20000000:
Read-Modify-Write operation
  Read the real data address (0x20000000)
  Modify the desired bit (retain other bits unchanged)
  Write the modified data back
Bit-band operation
  Directly set the bit by writing ‘1’ to address 0x2200000C, which is the alias address of the fourth bit of the 32-bit data at 0x20000000
    In effect, this single instruction is mapped to 2 bus transfers: read data from 0x20000000 to the buffer, and then write to 0x20000000 from the buffer with bit [3] set
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read
ORR.W R0, #0x8 ;Modify bit
STR R0, [R1] ;Write back
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write

## Slide 11: Bit-band Alias Address
Each bit of the 32-bit data is one-to-one mapped to the bit-band alias address
  For example, the fourth bit (bit [3]) of the data at 0x20000000 is mapped to the bit-band alias address at 0x2200000C
  Hence, to set bit [3] of the data at 0x20000000, we only need to write ‘1’ to address 0x2200000C
  In Cortex-M0+, there are two pre-defined bit-band alias regions: one for SRAM region, and one for peripherals region
0x20000000
0x20000004
0x20000008
Real 32-bit data address
0x22000000
0x22000080
0x22000100
0x2200000C
0x22000018
Bit-band alias address

## Slide 12: Bit-band Alias Address
SRAM region
  32MB memory space (0x22000000 – 0x23FFFFFF) is used as the bit-band alias region for 1MB data (0x20000000 – 0x200FFFFF)
Peripherals region
  32MB memory space (0x42000000 – 0x43FFFFFF) is used as the bit-band alias region for 1MB data (0x40000000 – 0x400FFFFF)
External RAM
Peripherals
SRAM
Code
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x20000000
0x20100000
0x22000000
0x23FFFFFF
0x21FFFFFF
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x40000000
0x40100000
0x42000000
0x43FFFFFF
0x41FFFFFF

## Slide 13: Benefits of Bit-Band Operations
Faster bit operations
Fewer instructions
Atomic operation, avoid hazards
  For example, if an interrupt is triggered and served during the Read-Modify-Write operations, and the interrupt service routine modifies the same data, a data conflict will occur
Interrupt occurs
Read data at 0x00
Modify bit [1]
Read data at 0x00
Modify bit [1]
Write data back
Write data back
Interrupt returns
Bit [1] modified by ISR is overwritten
by the main program
Interrupt Service Routine
Main program

## Slide 14: Cortex-M0+ Program Image
The program image in Cortex-M0+ contains
  Vector table -- includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP);
  C start-up routine;
  Program code – application code and data;
  C library code – program codes for C library functions.
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Initial MSP value
Reset vector
NMI vector
Hard fault vector
Reserved
PendSV
SysTick
External Interrupts
Reserved
SVCall

## Slide 15: Cortex-M0+ Program Image
After Reset, the processor:
  First reads the initial MSP value;
  Then reads the reset vector;
  Branches to the start of the programme execution address (reset handler);
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)

## Slide 16: Cortex-M0+ Endianness
Endian refers to the order of bytes stored in memory
  Big endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M0+ supports both little endian and big endian
However, Endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory

## Slide 17: ARM Cortex-M0+ Processor Instruction Set

## Slide 18: ARM and Thumb® Instruction Set
Early ARM instruction set
  32-bit instruction set, called the ARM instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in ARM7TDMI processor in 1995
  Provides a subset of the ARM instructions, giving better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%

## Slide 19: ARM and Thumb Instruction Set
Mix of ARM and Thumb-1 Instruction sets
  Benefit from both 32-bit ARM (high performance) and 16-bit Thumb-1 (high code density)
  A multiplexer is used to switch between two states: ARM state (32-bit) and Thumb state (16-bit), which requires a switching overhead
Thumb-2 instruction set
  Consists of both 32-bit Thumb instructions and original 16-bit Thumb-1 instruction sets
  Compared to 32-bit ARM instructions set, code size is reduced by ~26%, while keeping a similar performance
  Capable of handling all processing requirements in one operation state
Incoming
Instructions
Thumb remap
to ARM
ARM
Instruction
decoder
Instructions
Executing
T bit, 0: select ARM,
1: select Thumb
0
1

## Slide 20: Cortex-M0+ Instruction Set
Cortex-M0+ processor
  ARMv6-M architecture profile
  Includes all of the 16-bit Thumb instruction from ARMv7-M, excluding CBZ, CBNZ and IT.
  The 32-bit Thumb instructions BL, DMB, DSB, ISB, MRS and MSR.
  Supports 32-bit Thumb-2 instructions
  Possible to handle all processing requirements in one operation state (Thumb state)
  Compared with traditional ARM processors (use state switching), advantages include:
    No state switching overhead – both execution time and instruction space are saved
    No need to separate ARM code and Thumb code source files, which makes the development and maintenance of software easier
    Easier to get optimised efficiency and performance

## Slide 21: Cortex-M0+ Instruction Set
ARM assembly syntax:
  label
    mnemonic operand1, operand2, … ; Comments
  Label is used as a reference to an address location;
  Mnemonic is the name of the instruction;
  Operand1 is the destination of the operation;
  Operand2 is normally the source of the operation;
  Comments are written after “ ; ”, which does not affect the program;
  For example
  MOVS R3, #0x11 ;Set register R3 to 0x11
  Note that the assembly code can be assembled by either ARM assembler (armasm) or assembly tools from a variety of vendors (e.g. GNU tool chain). When using GNU tool chain, the syntax for labels and comments is slightly different

## Slide 22: Cortex-M0+ Instruction Set
Mnemonic | Operands | Brief description | Flags
ADCS | {Rd,} Rn, Rm | Add with Carry | N,Z,C,V
ADD{S} | {Rd,} Rn, <Rm¦#imm> | Add | N,Z,C,V
ADR | Rd, label | PC-relative Address to Register | 
ANDS | {Rd,} Rn, Rm | Bitwise AND | N,Z
ASRS | {Rd,} Rm, <Rs¦#imm> | Arithmetic Shift Right | N,Z,C
B{cc} | Label | Branch {conditionally} | 
BICS | {Rd,} Rn, Rm | Bit Clear | N,Z
BKPT | #imm | Breakpoint | 
BL | label | Branch with Link | 
BLX | Rm | Branch indirect with Link | 
BX | Rm | Branch indirect | 
CMN | Rn, Rm | Compare Negative | N,Z,C,V
CMP | Rn, <Rm¦ #imm> | Compare | N,Z,C,V
CPSID | i | Change Processor State, Disable Interrupts | 

## Slide 23: Cortex-M0+ Instruction Set
Mnemonic | Operands | Brief description | Flags
CPSIE | I | Change Processor State, Enable Interrupts | 
DMB |  | Data Memory Barrier | 
DSB |  | Data Synchronization Barrier | 
EORS | {Rd,} Rn, Rm | Exclusive OR | N,Z
ISB |  | Instruction Synchronization Barrier | 
LDM | Rn{!}, reglist | Load Multiple registers, increment after | 
LDR | Rt, label | Load Register from PC-relative address | 
LDR | Rt, [Rn, <Rm¦ #imm>] | Load Register with word | 
LDRB | Rt, [Rn, <Rm¦ #imm>] | Load Register with Byte | 
LDRH | Rt, [Rn, <Rm¦ #imm>] | Load Register with Halfword | 
LDRSB | Rt, [Rn, <Rm¦ #imm>] | Load Register with Signed Byte | 
LDRSH | Rt, [Rn, <Rm¦ #imm>] | Load Register with Signed Halfword | 
LSLS | {Rd, } Rn, <Rs¦ #imm> | Logical Shift Left | N,Z,C
LSRS | {Rd, } Rn, <Rs¦ #imm> | Logical Shift Right | N,Z,C

## Slide 24: Cortex-M0+ Instruction Set
Mnemonic | Operands | Brief description | Flags
MOV{S} | Rd, Rm | Move | N,Z
MRS | Rd, spec_reg | Move from Special Register to general register | 
MSR | spec_reg, Rm | Move from general register to Special Register | N,Z,C,V
MULS | Rd, Rn, Rm | Multiply, 32-bit result | N,Z
MVNS | Rd, Rm | Bitwise NOT | N,Z
NOP |  | No Operation | 
ORRS | {Rd,} Rn, Rm | Logical OR | N,Z
POP | reglist | Pop registers from stack | 
PUSH | reglist | Push registers onto stack | 
REV | Rd, Rm | Reverse byte order in a word | 
REV16 | Rd, Rm | Reverse byte order in each halfword | 
REVSH | Rd, Rm | Reverse byte order in bottom halfword and sign extend | 
RORS | {Rd, } Rn, Rs | Rotate Right | N,Z,C

## Slide 25: Cortex-M0+ Instruction Set
Mnemonic | Operands | Brief description | Flags
RSBS | {Rd,} Rn, #0 | Reverse Subtract | N,Z,C,V
SBCS | {Rd,} Rn, Rm | Subtract with Carry | N,Z,C,V
SEV |  | Send Event | 
STM | Rn!, reglist | Store Multiple registers, increment after | 
STR | Rt, [Rn, <Rm¦ #imm>] | Store Register as word | 
STRB | Rt, [Rn, <Rm¦ #imm>] | Store Register as byte | 
STRH | Rt, [Rn, <Rm¦ #imm>] | Store Register as Halfword | 
SUB{S} | {Rd, } Rn, <Rm¦ #imm> | Subtract | N,Z,C,V
SVC | #imm | Supervisor Call | 
SXTB | Rd, Rm | Sign extend byte | 
SXTH | Rd, Rm | Sign extend halfword | 
TST | Rn, Rm | Test | N,Z
UXTB | Rd, Rm | Zero extend a Byte | 
UXTH | Rd, Rm | Zero extend a Halfword | 

## Slide 26: Cortex-M0+ Instruction Set
Mnemonic | Operands | Brief description | Flags
WFE |  | Wait For Event | 
WFI |  | Wait For Interrupt | 
Note: full explanation of each instruction can be found in Cortex-M0+ Devices’ Generic User Guide (Ref-3)

## Slide 27: Cortex-M0+ Instruction Set
Mnemonic Extension | Meaning | Condition flags | Mnemonic Extension | Meaning | Condition flags
EQ | Equal | Z == 1 | HI | Unsigned Higher | C == 1 and Z == 0
NE | Not Equal | Z == 0 | LS | Unsigned lower or same | C == 0 or Z == 1
CS | Carry Set | C == 1 | GE | Signed greater than or equal | N == V
CC | Carry Clear | C == 0 | LT | Signed less than | N != V
MI | Minus, negative | N == 1 | GT | Signed greater than | Z == 0 or N != V
PL | Plus, positive or zero | N == 0 | None (AL) | Always (unconditional) | Any
VS | Overflow | V == 1 |  |  | 
VC | No Overflow | V == 0 |  |  | 
Condition codes
  Append to branch instruction (B) to make a conditional branch
  Full ARM instructions (not Thumb or Thumb-2) support conditional execution of arbitrary instructions
  Note: Carry bit = not-borrow for compares and subtractions

## Slide 28: Cortex-M0+ Instruction Set
Intrinsic functions
  ISO/IEC C code cannot directly access some Cortex-M0+ instructions. The following intrinsic functions can generate these instructions, provided by CMSIS and that might be provided by a C compiler. If a C compiler does not support an appropriate intrinsic function, you might have to use inline assembler to access the relevant instruction.
Instruction | CMSIS intrinsic function
CPSIE i | void __enable_irq(void)
CPSID i | void __disable_irq(void)
ISB | void __ISB(void)
DSB | void __DSB(void)
DMB | void __DMB(void)
NOP | void __NOP(void)
REV | uint32_t __REV(uint32_t int value)
REV16 | uint32_t __REV16(uint32_t int value)
REVSH | uint32_t __REVSH(uint32_t int value)
SEV | void __SEV(void)
WFE | void __WFE(void)
WFI | void __WFI(void)

## Slide 29: Useful Resources
Reference 1
  Cortex-M0+ Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0484c/DDI0484C_cortex_m0p_r0p1_trm.pdf
Reference 2
  Cortex-M0+ Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0662b/DUI0662B_cortex_m0p_r0p1_dgug.pdf
Reference 3
  Cortex-M0+ Processor Overview:
  http://www.arm.com/products/processors/cortex-m/cortex-m0plus.php