## Slide 1: Introduction to Embedded Systems
Notes: This course will introduce students to the fundamentals of embedded systems (ES). Embedded systems are, very briefly, task specialized microcomputer systems with chip embedded hardware components.
The selection, type, functionality, etc. of the embedded components varies among suppliers, chip series, etc. and need to be individually selected for each project to fit into given boundary conditions.
Within the course, the student will learn about basics terms and functionalities that are common for nearly all types of embedded systems.
In this module, a general overview is given.

## Slide 2: Module Syllabus
Introduction to Embedded Systems
  CPUs vs. MCUs vs. Embedded Systems
  Examples of Embedded Systems
  Options for Building Embedded Systems
  Features of Embedded Systems
Introduction to the Internet of Things (IoT)
  What is IoT?
  Why IoT?
  Challenges of IoT
Building Embedded Systems
  Building Embedded Systems Using MCUs
Notes: In this module we will define what an embedded system is and look at some examples. We will also introduce the Internet of Things and how it relates to embedded devices. Finally, we will take a brief look at options for building embedded systems, and the pros and cons of different methods.

## Slide 3: Introduction to Embedded Systems
What is an embedded system?
  Application-specific computer system
  Interacting with its environment
  Build into a larger system
  Often with real-time computing constraints
What is the motivation for building an embedded system?
  Better performance
  More functions and features
  Lower cost e.g. through automation
  More dependable
  Lower power
Embedded
System
Macroscopic view on a device level
Embedded Computer
Software
Hardware
Input from
Environment
Output to
Environment
User Interface
Link to
Other Systems
Microscopic view on a functionality level
Notes: An embedded system is a specialized computer system with chip embedded hardware. There are no standard definitions for an embedded systems, but principally it can be defined by a few attributes:
- Hybrid (pre-)processing and computing system
- Interacting with its environment
- Including a task specialized (internal) design
It is often part of a superordinate system, or integrated into a larger (virtual) system. A virtual system is a system that is not fixed (like a watch or car), but is set-up like a computer system with wireless connected components. Such virtual systems are sometimes also called ‘Internet-of-Things’ (IoT), which we will introduce later in this lecture.
The combination of a processing system, sensing physical input from its environment with physical sensors and communicating the result to its environment, is also called a ‘cyberphysical system’ (CPS). A comprehensive overview of CPS can be found at http://cyberphysicalsystems.org/
Usually embedded systems are designed because a repeating task has to be performed, either periodically or spontaneously, for low cost, low power, higher performance, etc.
Comment: It is advantageous to introduce the term and definition of a real-time system now, as its technical meaning is different from its colloquial use:
A real-time system is NOT a system doing things very fast and simulating ‘real-time’. It is a system that guarantees output within a defined period of time or interval without any infringement, independent of the length of the interval. For example, sending a signal once a day may be real-time if it is guaranteed within 24 hours.

## Slide 4: From a Processor to an Embedded System
Microprocessor (central processing unit, CPU)
  Typically defined as a single processor core that supports at least instruction fetching, decoding, and executing
  Normally can be used for general-purpose computing, but needs to be supported with memory and Input/Outputs (IOs)
Instruction fetcher
Instruction decoder
Register banks
ALU
Memory Interface
To memory
blocks
Microprocessor
Notes: The microprocessor is the central core of an embedded system and it performs the instruction cycle of fetching, decoding, and executing. It communicates with the external periphery, which consists of, at least, a memory interface. For an embedded system, there are many more components such as timers, interrupt handlers, and analog-digital-converters.

## Slide 5: Flynn’s Taxonomy
Data
Instructions
Single
Multiple
Single
Multiple
Single Instruction
Single Data
(SISD)
Multiple Instruction
Single Data
(MISD)
Single Instruction
Multiple Data
(SIMD)
Multiple Instruction
Multiple Data
(MIMD)
Majority of Embedded Systems
Notes: Flynn‘s taxonomy is a (historical) method for the organization of computer and algorithm types by data and instructions. It dates from the early 1970s.
Reference: FLYNN, M. Some computer organizations and their effectiveness, IEEE Trans. on Computers C-21, 9 (Sept. 1972), 948-960.
The basis of the taxonomy is the single operation instruction by instruction, fetching a single set of data. This is called a SISD.
If the same operation is performed on different sets of data, it is a SIMD; for example, a multicore or multiprocessor image processing system performing the same analysis on different parts of the picture parallel.
With multiple operations on the same data, it is a MISD; for example, a fault tolerant safety critical system, performing different independent algorithms on the same set of data.
Supercomputing systems are usually considered as MIMD, but this categorization depends on perspective. This is because every single part of the supercomputer may consider itself as SISD, and only the master unit, aggregating the computational result, may consider the whole system as MIMD.
Embedded systems are mostly classified as SISD or MISD.

## Slide 6: From a Processor to an Embedded System
Microcontroller (microcontroller unit, MCU)
  Typically has a single processor core
  Has memory blocks, digital IOs, analog IOs, and other basic peripherals
  Typically used for basic control purpose, such as embedded applications
Microprocessor (CPU)
Analog IO
Timer
Other Peripheral
Digital IO
Program Memory
Data Memory
System Bus
Microcontroller
Notes: Microcontrollers consist of a CPU, plus additional peripheral components. This means that:
The microprocessor is usually optimized for its task with regards to power and cost efficiency, so is usually a single core CPU.
On-chip memory components are designed and selected for the needs of the target application. This ranges from low-cost standard RAM and ROM to speed/cost/durability/energy efficiency optimized systems.
Additional hardware components for a controller architecture are selected according to its final purpose. They can include:
  - number and quality of input and output components
  - timers
  - interrupt structure
  - external buses
All components within a microcontroller are communicating via an internal system bus.

## Slide 7: Example of an Arm M4-MCU Architecture
Source: https://developer.arm.com/ip-products/subsystem/corstone-foundation-ip/cortex-m-system-design-kit
Notes: Shown here is a diagram of the Arm M4-MCU Architecture – outlining the different components and how they interact.

## Slide 8: From a Processor to an Embedded System
Embedded system
  Typically implemented using MCUs
  Often integrated into a larger mechanical or electrical system
  May have real-time constraints
Embedded
System
Notes: An embedded system usually contains one or many microcontrollers connected physically or virtually. Within this context, “virtually” means a generally intended, but not explicitly planned, interaction.
For example, an up-to-date mobile phone integrates the capability for wireless connections. It can principally work without it, but its systems can be virtually extended by an application using headphones, printers, etc. This is a virtual system establishing on-the-fly connections to other components depending on the software, context and peripherals.
Most parts of an embedded system are electrical components. An elementary part of an embedded system can also be the mechanical structure or the housing of the sensor, providing a key functionality of the embedded system.
Real time constraints (= guaranteed response times) may be an important part of an embedded system.

## Slide 9: Attributes of Embedded Systems
Interfacing with larger systems and environments
  Analog signals for reading sensors
    Typically use a voltage to represent a physical value
  Power electronics for driving motors, solenoids
  Digital interfaces for communicating with other digital devices
    Simple – switches
    Complex – displays
Concurrent and reactive behaviours
  Must respond to sequences and combinations of events
  Real-time systems have deadlines on responses
  Typically must perform multiple separate activities concurrently
Notes: There are many attributes that define an embedded system. In terms of a cyberphysical system (a system interacting with its environment), the most important selection criteria is the interface with its environment.
Criteria might include:
Types of signals to be read, such as analog or digital
Voltage range of system inputs and outputs
Power needed by the system itself and by its peripherals
Timing and multitasking/multithreading behaviour

## Slide 10: Attributes of Embedded Systems
Fault handling
  Many systems must operate independently for long periods of time
    Requires them to handle faults without crashing
  Often, fault-handling code is larger and more complex than the normal-case code
Diagnostics
  Help service personnel determine problems quickly
Notes: Note that aspects of fault handling and fault tolerance must also be covered.
It is important to know whether the system is allowed to crash, or whether fail safe modes are required. Perhaps independent parallel systems need to be set up, permanently communicating over a safe connection.
Additionally, there should be diagnostic mechanisms detecting system defects and handling them to prevent system crashes.

## Slide 11: Field Applications of Embedded Systems
Closed-loop control system
  Monitor and (pre)process a system state, adjust an output to maintain a desired set point (temperature, speed, direction, etc.)
  Remove noise, select desired signal features
Sequencing
  Step through different stages based on environment and system
Communications and networking
  Exchange information reliably and quickly
Part of a larger system
  Taking over very specialized functions as part of a larger system, e.g. fault handling, handling networking
Notes: The range of applications is infinitely large and only examples can be given:
Monitoring and pre-processing tasks of closed loop control systems are a very common task for embedded systems, as they are very small and cheap, and can be applied discretely nearly everywhere.
Setting up and managing small local networks. Here, usually slim and reduced protocols are used to reduce memory consumption and the need for power.
Example: Bluetooth Smart (= Bluetooth Low Energy), WLAN with limited functionality.
As a part of a larger system, very specialized sub functions are performed.

## Slide 12: Example Embedded System: Bike Computer
Input:
Wheel rotation
Mode key
Output:
Display speed and distance
Functions:
Speed measurement
Distance measurement
Constraints:
Size
Cost
Power and energy
Weight
Inputs:
Wheel rotation indicator
Mode key
Output:
Liquid crystal display
Use low-performance microcontroller:
  9-bit, 10 MIPS
Notes: A bike computer is one example of a small embedded system.
By means of a cyberphysical system, the bike computer senses wheel rotation, mostly magnetically, and outputs the calculated values such as speed, distance, and time to the user.
The constraints defined by user acceptance are primarily size/weight and cost, as well as battery lifetime -> power consumption. This means that the total system must be very cost-efficient. Fortunately, size, weight and cost usually coincide, and the only counteracting variable may be the processor performance.
The bike computer, as a weak real-time system, should begin between two sensor impulses. Occasionally, a speed update may be missing without the cyclist noticing.
This means that, if the computer is designed for a non-professional cyclist, it should at least be able to measure a range of up to 60km/h = 16.7 m/s for a racing bike. The circumference of the wheel of a racing bike is about 2m > 8 or 9 rotations/s.
Consequently, the system should be able to measure a frequency of 10 Hz without any complicated processing algorithms (time-difference-measurement, division, display). Therefore, it should not be a complicated task for the controller. This means that a very simple, low cost, low efficiency microcontroller can be selected.

## Slide 13: Example: Gasoline Automobile Engine Control Unit
Functions:
Fuel injection
Air intake setting
Spark timing
Exhaust gas circulation
Electronic throttle control
Knock control
Constraints:
Reliability in harsh environment
Cost
Size
Many inputs and outputs:
Discrete sensors and actuators
Network interface to rest of car
Use high-performance microcontroller:
E.g. 32-bit, 3 MB flash memory, 50-300 MHz
Notes: Another example of an embedded system is an engine control unit for a car:
In this example, the functional requirements and constraints are much greater than for the bike computer. Requirements such as spark timing need real-time calculations, as every spark is needed for correct operation of the motor. This means that every calculation must be finished at a defined point in time; otherwise, the engine is running rough.
Additional constraints are a high reliability in a harsh environment for relatively low cost. Furthermore, limited installation space requires a small device.
Many sensors and actuators have to be operated and networked to the rest of the car by the microcontroller. Consequently, a high-performance controller with a high reliability and a high speed is needed.

## Slide 14: Introduction to the Internet of Things (IoT)
IoT generally refers to a world in which a large range of objects are addressable via a network
IoT
Why IoT?
Items can have more functionality and become more intelligent
Items can be managed more easily
More information becomes available
Objects can include:
Smart buildings and home appliances
  Fridges, TVs, cookers
Civil engineering structures
  Bridges, railways
Wearable devices
  Smart watches, glasses
Medical devices
  Smart inhaler, embedded pills
Notes: The Internet of Things (IoT) is a special form or application of embedded systems. Wherever possible or necessary, a physical device will be equipped with a microcontroller, sensors and communication interface, to connect with its environment and network with the whole world.
The overarching goal of IoT is that everything should be able to communicate with everything: washing machines with buildings, fridges with grocery stores, personal daily schedules with traffic management systems. This will make things more efficient and make better use of resources.

## Slide 15: Internet of Things: Why Now?
Embedded chips are becoming:
  Cheaper
  Smaller
  Lower power
Energy harvesting
Communication is becoming faster and more efficient
Number of embedded systems
Price
Notes: The IoT phenomenon is enabled by vast technical development in embedded chips. With smaller packages of embedded systems and more efficient production, prices can drop, allowing the number of applications and required systems to increase. Consequently, production becomes more efficient, prices drop, units increase, and innovation is promoted.
Additionally, smaller chip systems consume less power, again opening possibilities for new applications.

## Slide 16: Challenges to the Internet of Things
Large number of chips required
  Chips have become even cheaper and smaller
Big data demand
  Large volume of data will be generated, data centre storage needs to be increased
Computation requirement
  High performance e.g. for cloud computing
Power consumption
  Low power chips, longer battery life
Security
  Large amount of private data needs to be protected
Standards
  Official standards are required, such as network protocols
Notes: But there are still challenges to solve in order to get a real Internet of Things up and running:
Even the smallest controllers have a footprint of several mm^2 and have a price of some ten cents, making them too large and too expensive to use everywhere.
The vast amount of data produced must be handled.
Batteries are not long-lasting enough for permanently used systems. The current strategy for the prolongation of battery life is to let the controllers sleep as much as possible, but this contradicts the concept of permanent use.
Security becomes an issue as more processors and controllers come up and network spontaneously. One infringed element may corrupt a whole system.
As soon as everything starts communicating with everything, official standards are required.

## Slide 17: Options for Building Embedded Systems
Dedicated
Hardware
Software Running on Generic Hardware
Implementation | Design Cost | Unit Cost | Upgrades & Bug Fixes | Size | Weight | Power | System Speed
Discrete logic | low | mid | hard | large | high | ? | very fast
ASIC | high ($500K/ mask set) | very low | hard | tiny – 1 die | very low | low | extremely fast
Programmable logic – FPGA, PLD | low to mid | mid | easy | small | low | medium to high | very fast
Microprocessor + memory + peripherals | low to mid | mid | easy | small to medium | low to moderate | medium | moderate
Microcontroller (int. memory & peripherals) | low | mid to low | easy | small | low | medium | slow to moderate
Embedded PC | low | high | easy | medium | moderate to high | medium to high | fast
Microcontroller based embedded system
Notes: Although the term ‘embedded system’ is mostly used for microcontroller-based systems, it is not restricted to just that. ‘Embedded system’ generally stands for systems with as much functionality as possible embedded into fewer components.
It covers the range from discrete hardware components such as transistors, resistors and capacitors to fully embedded PCs. Somewhere in between are microprocessors with dedicated hardware elements and microcontrollers with chip embedded hardware.
The table above shows the pros and cons of different types of embedded systems.

## Slide 18: Benefits of Microcontroller-based Embedded Systems
Greater performance and efficiency
  Software makes it possible to provide sophisticated control
Lower costs for mixed signal-processing systems
  Less expensive components can be used
  Manufacturing costs reduced
  Operating costs reduced
  Maintenance costs reduced
More features
  May not be possible or practical with other approaches
Better dependability
  Adaptive system which can compensate for failures
  Better diagnostics to improve repair time
Notes: It is obvious that a microcontroller-based embedded system has numerous advantages:
Software-based applications provide better flexibility than pure hardware and are more easily adapted to the needs of system changes.
With an intelligent partition of the system into hardware and software components, the total system cost can be minimized. A base rule for the best ratio between upfront engineering expenses and production/lifetime cost is: The higher the quantity, the more engineering effort may be spent on the perfect system partition to reduce the unit cost.
The feature extension of the system is usually only possible with a microcontroller-based system. However, the more effort is spent on system optimization, the less redundancy such as memory, clock cycles, on-chip components, is left for later features.
Failures can be more easily detected, debugged, and compensated with a microcontroller-based embedded system.

## Slide 19: Impact of Constraints
Microcontrollers used (rather than microprocessors)
  Include peripherals to interface with other devices, respond efficiently
  On-chip RAM, ROM reduce circuit board complexity and cost
Programming language
  Programmed in the C language rather than Java (resulting in smaller and faster code – less expensive MCU)
  Some performance-critical code may be in assembly language
Operating system
  Typically no OS, but instead a simple scheduler
  If OS is used, it is likely to be a lean RTOS
Notes: Alongside the benefits of microcontroller-based embedded systems, there are difficulties in handling them:
As peripherals are already integrated on chip, they are usually operated in a very unique way, differing between every controller type. This reduces manufacturing costs but increases the engineering costs for design, development and debugging. So the board and design complexity is reduced but the chip-and-coding complexity is increased.
Programming is mostly done in C or assembly language. This is most the most efficient use of code and programming overhead. C++, with all the benefits of object-oriented programming, is sometimes used in larger embedded systems, with a major focus on algorithm-centred applications. However, task, interrupt, and time-slice-based applications are still best in C and assembly as they make it easier to control the required clock cycles per operation.
Although some systems are also programmed in interpreting languages such as Basic or Java, this is the exception, because code optimization is nearly impossible.
Even operating systems are very uncommon for embedded systems. Although they make things much easier, their overheads extend code size and reduces transparency about what is really happening inside the controller.

## Slide 20: Summary: Building Embedded Systems using MCUs
In most embedded systems, MCUs are the best solution as they offer:
  Low development and manufacturing cost
  Easy porting and updating
  Light footprint
  Relatively low power consumption
  Satisfactory performance for low-end products
In the upcoming labs, we will learn some fundamentals of developing for embedded systems. This will be achieved using an easy-to-start MCU design suite – the Mbed platform.
Notes: So microcontroller units (MCU) are the best choice for the development of embedded systems as they are:
Cheap
Flexible
Available in multiple configurations
Low power consumption
Usually there are special development environments required, supporting each single processor type for uploading code and debugging.
To reduce learning time and effort, this course will use the mbed platform for program development of embedded code.

## Slide 21: Coming Next
Knowledge of embedded systems
  Hardware mechanisms
    Introducing the Arm Cortex-M architecture
    Use interrupts for low power design
  Software programming
    Programming basics: C/C++ programming
    Introducing the Mbed platform
    Learn to use software libraries: Mbed API
Notes: In the next modules – we will explore a number of embedded system related areas. This includes the Mbed platform, the Arm Cortex-M processor architecture, interrupts and more.

## Slide 22: Coming Next
Develop your own embedded systems
  Analog IOs: ADC, DAC, PWM
  Serial communications: UART, I2C, SPI
  Advanced serial communication: USB, CAN, Bluetooth LE
  Network: Ethernet, TCP/IP, HTTP
  Real-time operating system (RTOS)
  Prototyping applications for IoT

## Slide 23: Resources
Official Mbed website: https://www.mbed.com/en/
Notes: For more information about the Mbed platform, visit this site.