## Slide 1: The ARM Cortex-M4 Processor Architecture

## Slide 2: Module Syllabus
Cortex-M4 Memory Map
  Cortex-M4 Memory Map
  Bit-band Operations
  Cortex-M4 Program Image and Endianness
ARM Cortex-M4 Processor Instruction Set
  ARM and Thumb Instruction Set
  Cortex-M4 Instruction Set

## Slide 3: ARM Cortex-M4 Processor Memory Map

## Slide 4: Cortex-M4 Memory Map
The Cortex-M4 processor has 4 GB of memory address space
  Support for bit-band operation (detailed later)
The 4GB memory space is architecturally defined as a number of regions
  Each region is given for recommended usage
  Easy for software programmer to port between different devices
Nevertheless, despite of the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus

## Slide 5: Cortex-M4 Memory Map
Private peripherals
e.g. NVIC, SCS
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH
Vendor specific
Memory
External device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
(PPB)
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM table
External PPB
Embedded trace macrocell
Trace port interface unit
Reserved
System Control Space, including
Nested Vectored Interrupt
Controller (NVIC)
Reserved
Fetch patch and breakpoint unit
Data watchpoint and trace unit
Instrumentation trace macrocell
External PPB
Internal PPB

## Slide 6: Cortex-M4 Memory Map
Code Region
  Primarily used to store program code
  Can also be used for data memory
  On-chip memory, such as on-chip FLASH
SRAM Region
  Primarily used to store data, such as heaps and stacks
  Can also be used for program code
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM or other types
Peripheral Region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals
  On-chip peripherals

## Slide 7: Cortex-M4 Memory Map
External RAM Region
  Primarily used to store large data blocks, or memory caches
  Off-chip memory, slower than on-chip SRAM region
External Device Region
  Primarily used to map to external devices
  Off-chip devices, such as SD card
Internal Private Peripheral Bus (PPB)
  Used inside the processor core for internal control
  Within PPB, a special range of memory is defined as System Control Space (SCS)
  The Nested Vectored Interrupt Controller (NVIC) is part of SCS

## Slide 8: Cortex-M4 Memory Map Example
AHB bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M4
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon

## Slide 9: Bit-band Operations
Bit-band operation allows a single load/store operation to access a single bit in the memory, for example, to change a single bit of one 32-bit data:
  Normal operation without bit-band (read-modify-write)
          Read the value of 32-bit data
          Modify a single bit of the 32-bit value (keep other bits unchanged)
          Write the value back to the address
  Bit-band operation
          Directly write a single bit (0 or 1) to the “bit-band alias address” of the data
Bit-band alias address
  Each bit-band alias address is mapped to a real data address
  When writing to the bit-band alias address, only a single bit of the data will be changed

## Slide 10: Bit-band Operation Example
For example, in order to set bit[3] in word data in address 0x20000000:
Read-Modify-Write operation
  Read the real data address (0x20000000)
  Modify the desired bit (retain other bits unchanged)
  Write the modified data back
Bit-band operation
  Directly set the bit by writing ‘1’ to address 0x2200000C, which is the alias address of the fourth bit of the 32-bit data at 0x20000000
          In effect, this single instruction is mapped to 2 bus transfers: read data from 0x20000000 to the buffer, and then write to 0x20000000 from the buffer with bit [3] set
;Read-Modify-Write Operation
LDR R1, =0x20000000 ;Setup address
LDR R0, [R1] ;Read
ORR.W R0, #0x8 ;Modify bit
STR R0, [R1] ;Write back
;Bit-band Operation
LDR R1, =0x2200000C ;Setup address
MOV R0, #1 ;Load data
STR R0, [R1] ;Write

## Slide 11: Bit-band Alias Address
Each bit of the 32-bit data is one-to-one mapped to the bit-band alias address
  For example, the fourth bit (bit [3]) of the data at 0x20000000 is mapped to the bit-band alias address at 0x2200000C
  Hence, to set bit [3] of the data at 0x20000000, we only need to write ‘1’ to address 0x2200000C
  In Cortex-M4, there are two pre-defined bit-band alias regions: one for SRAM region, and one for peripherals region
0x20000000
0x20000004
0x20000008
Real 32-bit data address
0x22000000
0x22000080
0x22000100
0x2200000C
0x22000018
Bit-band alias address

## Slide 12: Bit-band Alias Address
SRAM region
  32MB memory space (0x22000000 – 0x23FFFFFF) is used as the bit-band alias region for 1MB data (0x20000000 – 0x200FFFFF)
Peripherals region
  32MB memory space (0x42000000 – 0x43FFFFFF) is used as the bit-band alias region for 1MB data (0x40000000 – 0x400FFFFF)
External RAM
Peripherals
SRAM
Code
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x20000000
0x20100000
0x22000000
0x23FFFFFF
0x21FFFFFF
1MB Bit-band region
32MB Bit-band alias
31MB non-bit-band region
0x40000000
0x40100000
0x42000000
0x43FFFFFF
0x41FFFFFF

## Slide 13: Benefits of Bit-Band Operations
Faster bit operations
Fewer instructions
Atomic operation, avoid hazards
  For example, if an interrupt is triggered and served during the Read-Modify-Write operations, and the interrupt service routine modifies the same data, a data conflict will occur
Interrupt occurs
Read data at 0x00
Modify bit [1]
Read data at 0x00
Modify bit [1]
Write data back
Write data back
Interrupt returns
Bit [1] modified by ISR is overwritten
by the main program
Interrupt Service Routine
Main program

## Slide 14: Cortex-M4 Program Image
The program image in Cortex-M4 contains
  Vector table -- includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP);
  C start-up routine;
  Program code – application code and data;
  C library code – program codes for C library functions.
0x00000000
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Initial MSP value
Reset vector
NMI vector
Hard fault vector
MemManage fault
Reserved
PendSV
SysTick
External Interrupts
Bus fault
Usage fault
Reserved
SVCall
Debug monitor

## Slide 15: Cortex-M4 Program Image
After Reset, the processor:
  First reads the initial MSP value;
  Then reads the reset vector;
  Branches to the start of the programme execution address (reset handler);
  Subsequently executes program instructions
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)

## Slide 16: Cortex-M4 Endianness
Endian refers to the order of bytes stored in memory
  Big endian: lowest byte of a word-size data is stored in bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in bit 24 to bit 31
Cortex-M4 supports both little endian and big endian
However, Endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory

## Slide 17: ARM Cortex-M4 Processor Instruction Set

## Slide 18: ARM and Thumb® Instruction Set
Early ARM instruction set
  32-bit instruction set, called the ARM instructions
  Powerful and good performance
  Larger program memory compared to 8-bit and 16-bit processors
  Larger power consumption
Thumb-1 instruction set
  16-bit instruction set, first used in ARM7TDMI processor in 1995
  Provides a subset of the ARM instructions, giving better code density compared to 32-bit RISC architecture
  Code size is reduced by ~30%, but performance is also reduced by ~20%

## Slide 19: ARM and Thumb Instruction Set
Mix of ARM and Thumb-1 Instruction sets
  Benefit from both 32-bit ARM (high performance) and 16-bit Thumb-1 (high code density)
  A multiplexer is used to switch between two states: ARM state (32-bit) and Thumb state (16-bit), which requires a switching overhead
Thumb-2 instruction set
  Consists of both 32-bit Thumb instructions and original 16-bit Thumb-1 instruction sets
  Compared to 32-bit ARM instructions set, code size is reduced by ~26%, while keeping a similar performance
  Capable of handling all processing requirements in one operation state
Incoming
Instructions
Thumb remap
to ARM
ARM
Instruction
decoder
Instructions
Executing
T bit, 0: select ARM,
1: select Thumb
0
1

## Slide 20: Cortex-M4 Instruction Set
Cortex-M4 processor
  ARMv7-M architecture
  Supports 32-bit Thumb-2 instructions
  Possible to handle all processing requirements in one operation state (Thumb state)
  Compared with traditional ARM processors (use state switching), advantages include:
          No state switching overhead – both execution time and instruction space are saved
          No need to separate ARM code and Thumb code source files, which makes the development and maintenance of software easier
          Easier to get optimised efficiency and performance

## Slide 21: Cortex-M4 Instruction Set
ARM assembly syntax:
  label
    mnemonic operand1, operand2, … ; Comments
  Label is used as a reference to an address location;
  Mnemonic is the name of the instruction;
  Operand1 is the destination of the operation;
  Operand2 is normally the source of the operation;
  Comments are written after “ ; ”, which does not affect the program;
  For example
  MOVS R3, #0x11 ;Set register R3 to 0x11
  Note that the assembly code can be assembled by either ARM assembler (armasm) or assembly tools from a variety of vendors (e.g. GNU tool chain). When using GNU tool chain, the syntax for labels and comments is slightly different

## Slide 22: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
ADC, ADCS | {Rd,} Rn, Op2 | Add with Carry | N,Z,C,V
ADD, ADDS | {Rd,} Rn, Op2 | Add | N,Z,C,V
ADD, ADDW | {Rd,} Rn, #imm12 | Add | N,Z,C,V
ADR | Rd, label | Load PC-relative Address | 
AND, ANDS | {Rd,} Rn, Op2 | Logical AND | N,Z,C
ASR, ASRS | Rd, Rm, <Rs¦#n> | Arithmetic Shift Right | N,Z,C
B | label | Branch | 
BFC | Rd, #lsb, #width | Bit Field Clear | 
BFI | Rd, Rn, #lsb, #width | Bit Field Insert | 
BIC, BICS | {Rd,} Rn, Op2 | Bit Clear | N,Z,C
BKPT | #imm | Breakpoint | 
BL | label | Branch with Link | 
BLX | Rm | Branch indirect with Link | 
BX | Rm | Branch indirect | 

## Slide 23: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
CBNZ | Rn, label | Compare and Branch if Non Zero | 
CBZ | Rn, label | Compare and Branch if Zero | 
CLREX |  | Clear Exclusive | 
CLZ | Rd, Rm | Count Leading Zeros | 
CMN | Rn, Op2 | Compare Negative | N,Z,C,V
CMP | Rn, Op2 | Compare | N,Z,C,V
CPSID | i | Change Processor State, Disable Interrupts | 
CPSIE | i | Change Processor State, Enable Interrupts | 
DMB |  | Data Memory Barrier | 
DSB |  | Data Synchronization Barrier | 
EOR, EORS | {Rd,} Rn, Op2 | Exclusive OR | N,Z,C
ISB | - | Instruction Synchronization Barrier | 

## Slide 24: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
IT |  | If-Then condition block | 
LDM | Rn{!}, reglist | Load Multiple registers, increment after | 
LDMDB, LDMEA | Rn{!}, reglist | Load Multiple registers, decrement before | 
LDMFD, LDMIA | Rn{!}, reglist | Load Multiple registers, increment after | 
LDR | Rt, [Rn, #offset] | Load Register with word | 
LDRB, LDRBT | Rt, [Rn, #offset] | Load Register with byte | 
LDRD | Rt, Rt2, [Rn, #offset] | Load Register with two bytes | 
LDREX | Rt, [Rn, #offset] | Load Register Exclusive | 
LDREXB | Rt, [Rn] | Load Register Exclusive with Byte | 
LDREXH | Rt, [Rn] | Load Register Exclusive with Halfword | 
LDRH, LDRHT | Rt, [Rn, #offset] | Load Register with Halfword | 

## Slide 25: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
LDRSB, LDRSBT | Rt, [Rn, #offset] | Load Register with Signed Byte | 
LDRSH, LDRSHT | Rt, [Rn, #offset] | Load Register with Signed Halfword | 
LDRT | Rt, [Rn, #offset] | Load Register with word | 
LSL, LSLS | Rd, Rm, <Rs¦#n> | Logical Shift Left | N,Z,C
LSR, LSRS | Rd, Rm, <Rs¦#n> | Logical Shift Right | N,Z,C
MLA | Rd, Rn, Rm, Ra | Multiply with Accumulate, 32-bit result | 
MLS | Rd, Rn, Rm, Ra | Multiply and Subtract, 32-bit result | 
MOV, MOVS | Rd, Op2 | Move | N,Z,C
MOVT | Rd, #imm16 | Move Top | 
MOVW, MOV | Rd, #imm16 | Move 16-bit constant | N,Z,C
MRS | Rd, spec_reg | Move from Special Register to general register | 
MSR | spec_reg, Rm | Move from general register to Special Register | N,Z,C,V

## Slide 26: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
MUL, MULS | {Rd,} Rn, Rm | Multiply, 32-bit result | N,Z
MVN, MVNS | Rd, Op2 | Move NOT | N,Z,C
NOP |  | No Operation | 
ORN, ORNS | {Rd,} Rn, Op2 | Logical OR NOT | N,Z,C
ORR, ORRS | {Rd,} Rn, Op2 | Logical OR | N,Z,C
PKHTB, PKHBT | {Rd, } Rn, Rm, Op2 | Pack Halfword | 
POP | reglist | Pop registers from stack | 
PUSH | reglist | Push registers onto stack | 
QADD | {Rd, } Rn, Rm | Saturating double and Add | Q
QADD16 | {Rd, } Rn, Rm | Saturating Add 16 | 
QADD8 | {Rd, } Rn, Rm | Saturating Add 8 | 

## Slide 27: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
QASX | {Rd, } Rn, Rm | Saturating Add and Subtract with Exchange | 
QDADD | {Rd, } Rn, Rm | Saturating Add | Q
QDSUB | {Rd, } Rn, Rm | Saturating double and Subtract | Q
QSAX | {Rd, } Rn, Rm | Saturating Subtract and Add with Exchange | 
QSUB | {Rd, } Rn, Rm | Saturating Subtract | Q
QSUB16 | {Rd, } Rn, Rm | Saturating Subtract 16 | 
QSUB8 | {Rd, } Rn, Rm | Saturating Subtract 8 | 
RBIT | Rd, Rn | Reverse Bits | 
REV | Rd, Rn | Reverse byte order in a word | 
REV16 | Rd, Rn | Reverse byte order in each halfword | 
REVSH | Rd, Rn | Reverse byte order in bottom halfword and sign extend | 
ROR, RORS | Rd, Rm, <Rs¦#n> | Rotate Right | N,Z,C

## Slide 28: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
RRX, RRXS | Rd, Rm | Rotate Right with Extend | N,Z,C
RSB, RSBS | {Rd,} Rn, Op2 | Reverse Subtract | N,Z,C,V
SADD16 | {Rd, } Rn, Rm | Signed Add 16 | GE
SADD8 | {Rd, } Rn, Rm | Signed Add 8 | GE
SASX | {Rd, } Rn, Rm | Signed Add and Subtract with Exchange | GE
SBC, SBCS | {Rd,} Rn, Op2 | Subtract with Carry | N,Z,C,V
SBFX | Rd, Rn, #lsb, #width | Signed Bit Field Extract | 
SDIV | {Rd,} Rn, Rm | Signed Divide | 
SEV |  | Send Event | 
SHADD16 | {Rd,} Rn, Rm | Signed Halving Add 16 | 
SHADD8 | {Rd,} Rn, Rm | Signed Halving Add 8 | 
SHASX | {Rd,} Rn, Rm | Signed Halving Add and Subtract with Exchange | 

## Slide 29: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SHSAX | {Rd,} Rn, Rm | Signed Halving Subtract and Add with Exchange | 
SHSUB16 | {Rd,} Rn, Rm | Signed Halving Subtract 16 | 
SHSUB8 | {Rd,} Rn, Rm | Signed Halving Subtract 8 | 
SMLABB, SMLABT, SMLATB, SMLATT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate Long (halfwords) | Q
SMLAD, SMLADX | Rd, Rn, Rm, Ra | Signed Multiply Accumulate Dual | Q
SMLAL | RdLo, RdHi, Rn, Rm | Signed Multiply with Accumulate (32 x 32 + 64), 64-bit result | 
SMLALBB, SMLALBT, SMLALTB, SMLALTT | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long, halfwords | 
SMLALD, SMLALDX | RdLo, RdHi, Rn, Rm | Signed Multiply Accumulate Long Dual | 
SMLAWB, SMLAWT | Rd, Rn, Rm, Ra | Signed Multiply Accumulate, word by halfword | Q
SMLSD | Rd, Rn, Rm, Ra | Signed Multiply Subtract Dual | Q
SMLSLD | RdLo, RdHi, Rn, Rm | Signed Multiply Subtract Long Dual | 
SMMLA | Rd, Rn, Rm, Ra | Signed Most significant word Multiply Accumulate | 

## Slide 30: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SMMLS, SMMLR | Rd, Rn, Rm, Ra | Signed Most significant word Multiply Subtract | 
SMMUL, SMMULR | {Rd,} Rn, Rm | Signed Most significant word Multiply | 
SMUAD | {Rd,} Rn, Rm | Signed dual Multiply Add | Q
SMULBB, SMULBT SMULTB, SMULTT | {Rd,} Rn, Rm | Signed Multiply (halfwords) | 
SMULL | RdLo, RdHi, Rn, Rm | Signed Multiply (32 x 32), 64-bit result | 
SMULWB, SMULWT | {Rd,} Rn, Rm | Signed Multiply word by halfword | 
SMUSD, SMUSDX | {Rd,} Rn, Rm | Signed dual Multiply Subtract | 
SSAT | Rd, #n, Rm {,shift #s} | Signed Saturate | Q
SSAT16 | Rd, #n, Rm | Signed Saturate 16 | Q
SSAX | {Rd,} Rn, Rm | Signed Subtract and Add with Exchange | GE
SSUB16 | {Rd,} Rn, Rm | Signed Subtract 16 | 
SSUB8 | {Rd,} Rn, Rm | Signed Subtract 8 | 

## Slide 31: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
STM | Rn{!}, reglist | Store Multiple registers, increment after | 
STMDB, STMEA | Rn{!}, reglist | Store Multiple registers, decrement before | 
STMFD, STMIA | Rn{!}, reglist | Store Multiple registers, increment after | 
STR | Rt, [Rn, #offset] | Store Register word | 
STRB, STRBT | Rt, [Rn, #offset] | Store Register byte | 
STRD | Rt, Rt2, [Rn, #offset] | Store Register two words | 
STREX | Rd, Rt, [Rn, #offset] | Store Register Exclusive | 
STREXB | Rd, Rt, [Rn] | Store Register Exclusive Byte | 
STREXH | Rd, Rt, [Rn] | Store Register Exclusive Halfword | 
STRH, STRHT | Rt, [Rn, #offset] | Store Register Halfword | 
STRT | Rt, [Rn, #offset] | Store Register word | 
SUB, SUBS | {Rd,} Rn, Op2 | Subtract | N,Z,C,V

## Slide 32: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
SUB, SUBW | {Rd,} Rn, #imm12 | Subtract | N,Z,C,V
SVC | #imm | Supervisor Call | 
SXTAB | {Rd,} Rn, Rm,{,ROR #} | Extend 8 bits to 32 and add | 
SXTAB16 | {Rd,} Rn, Rm,{,ROR #} | Dual extend 8 bits to 16 and add | 
SXTAH | {Rd,} Rn, Rm,{,ROR #} | Extend 16 bits to 32 and add | 
SXTB16 | {Rd,} Rm {,ROR #n} | Signed Extend Byte 16 | 
SXTB | {Rd,} Rm {,ROR #n} | Sign extend a byte | 
SXTH | {Rd,} Rm {,ROR #n} | Sign extend a halfword | 
TBB | [Rn, Rm] | Table Branch Byte | 
TBH | [Rn, Rm, LSL #1] | Table Branch Halfword | 
TEQ | Rn, Op2 | Test Equivalence | N,Z,C
TST | Rn, Op2 | Test | N,Z,C

## Slide 33: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UADD16 | {Rd,} Rn, Rm | Unsigned Add 16 | GE
UADD8 | {Rd,} Rn, Rm | Unsigned Add 8 | GE
USAX | {Rd,} Rn, Rm | Unsigned Subtract and Add with Exchange | GE
UHADD16 | {Rd,} Rn, Rm | Unsigned Halving Add 16 | 
UHADD8 | {Rd,} Rn, Rm | Unsigned Halving Add 8 | 
UHASX | {Rd,} Rn, Rm | Unsigned Halving Add and Subtract with Exchange | 
UHSAX | {Rd,} Rn, Rm | Unsigned Halving Subtract and Add with Exchange | 
UHSUB16 | {Rd,} Rn, Rm | Unsigned Halving Subtract 16 | 
UHSUB8 | {Rd,} Rn, Rm | Unsigned Halving Subtract 8 | 
UBFX | Rd, Rn, #lsb, #width | Unsigned Bit Field Extract | 
UDIV | {Rd,} Rn, Rm | Unsigned Divide | 
UMAAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply Accumulate Accumulate Long (32 x 32 + 32 +32), 64-bit result | 

## Slide 34: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UMLAL | RdLo, RdHi, Rn, Rm | Unsigned Multiply with Accumulate (32 x 32 + 64), 64-bit result | 
UMULL | RdLo, RdHi, Rn, Rm | Unsigned Multiply (32 x 32), 64-bit result | 
UQADD16 | {Rd,} Rn, Rm | Unsigned Saturating Add 16 | 
UQADD8 | {Rd,} Rn, Rm | Unsigned Saturating Add 8 | 
UQASX | {Rd,} Rn, Rm | Unsigned Saturating Add and Subtract with Exchange | 
UQSAX | {Rd,} Rn, Rm | Unsigned Saturating Subtract and Add with Exchange | 
UQSUB16 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 16 | 
UQSUB8 | {Rd,} Rn, Rm | Unsigned Saturating Subtract 8 | 
USAD8 | {Rd,} Rn, Rm | Unsigned Sum of Absolute Differences | 
USADA8 | {Rd,} Rn, Rm, Ra | Unsigned Sum of Absolute Differences and Accumulate | 
USAT | Rd, #n, Rm {,shift #s} | Unsigned Saturate | Q
USAT16 | Rd, #n, Rm | Unsigned Saturate 16 | Q

## Slide 35: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
UASX | {Rd,} Rn, Rm | Unsigned Add and Subtract with Exchange | GE
USUB16 | {Rd,} Rn, Rm | Unsigned Subtract 16 | GE
USUB8 | {Rd,} Rn, Rm | Unsigned Subtract 8 | GE
UXTAB | {Rd,} Rn, Rm,{,ROR #} | Rotate, extend 8 bits to 32 and Add | 
UXTAB16 | {Rd,} Rn, Rm,{,ROR #} | Rotate, dual extend 8 bits to 16 and Add | 
UXTAH | {Rd,} Rn, Rm,{,ROR #} | Rotate, unsigned extend and Add Halfword | 
UXTB | {Rd,} Rm {,ROR #n} | Zero extend a Byte | 
UXTB16 | {Rd,} Rm {,ROR #n} | Unsigned Extend Byte 16 | 
UXTH | {Rd,} Rm {,ROR #n} | Zero extend a Halfword | 
VABS.F32 | Sd, Sm | Floating-point Absolute | 
VADD.F32 | {Sd,} Sn, Sm | Floating-point Add | 
VCMP.F32 | Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero | FPSCR

## Slide 36: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VCMPE.F32 | Sd, <Sm ¦ #0.0> | Compare two floating-point registers, or one floating-point register and zero with Invalid Operation check | FPSCR
VCVT.S32.F32 | Sd, Sm | Convert between floating-point and integer | 
VCVT.S16.F32 | Sd, Sd, #fbits | Convert between floating-point and fixed point | 
VCVTR.S32.F32 | Sd, Sm | Convert between floating-point and integer with rounding | 
VCVT<B¦H>.F32.F16 | Sd, Sm | Converts half-precision value to single-precision | 
VCVTT<B¦T>.F32.F16 | Sd, Sm | Converts single-precision register to half-precision | 
VDIV.F32 | {Sd,} Sn, Sm | Floating-point Divide | 
VFMA.F32 | {Sd,} Sn, Sm | Floating-point Fused Multiply Accumulate | 
VFNMA.F32 | {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Accumulate | 
VFMS.F32 | {Sd,} Sn, Sm | Floating-point Fused Multiply Subtract | 
VFNMS.F32 | {Sd,} Sn, Sm | Floating-point Fused Negate Multiply Subtract | 
VLDM.F<32¦64> | Rn{!}, list | Load Multiple extension registers | 

## Slide 37: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VLDR.F<32¦64> | <Dd¦Sd>, [Rn] | Load an extension register from memory | 
VLMA.F32 | {Sd,} Sn, Sm | Floating-point Multiply Accumulate | 
VLMS.F32 | {Sd,} Sn, Sm | Floating-point Multiply Subtract | 
VMOV.F32 | Sd, #imm | Floating-point Move immediate | 
VMOV | Sd, Sm | Floating-point Move register | 
VMOV | Sn, Rt | Copy ARM core register to single precision | 
VMOV | Sm, Sm1, Rt, Rt2 | Copy 2 ARM core registers to 2 single precision | 
VMOV | Dd[x], Rt | Copy ARM core register to scalar | 
VMOV | Rt, Dn[x] | Copy scalar to ARM core register | 
VMRS | Rt, FPSCR | Move FPSCR to ARM core register or APSR | N,Z,C,V
VMSR | FPSCR, Rt | Move to FPSCR from ARM Core register | FPSCR
VMUL.F32 | {Sd,} Sn, Sm | Floating-point Multiply | 

## Slide 38: Cortex-M4 Instruction Set
Mnemonic | Operands | Brief description | Flags
VNEG.F32 | Sd, Sm | Floating-point Negate | 
VNMLA.F32 | Sd, Sn, Sm | Floating-point Multiply and Add | 
VNMLS.F32 | Sd, Sn, Sm | Floating-point Multiply and Subtract | 
VNMUL | {Sd,} Sn, Sm | Floating-point Multiply | 
VPOP | list | Pop extension registers | 
VPUSH | list | Push extension registers | 
VSQRT.F32 | Sd, Sm | Calculates floating-point Square Root | 
VSTM | Rn{!}, list | Floating-point register Store Multiple | 
VSTR.F<32¦64> | Sd, [Rn] | Stores an extension register to memory | 
VSUB.F<32¦64> | {Sd,} Sn, Sm | Floating-point Subtract | 
WFE |  | Wait For Event | 
WFI |  | Wait For Interrupt | 
Note: full explanation of each instruction can be found in Cortex-M4 Devices’ Generic User Guide (Ref-4)

## Slide 39: Cortex-M4 Instruction Set
Cortex-M4 Suffix
  Some instructions can be followed by suffixes to update processor flags or execute the instruction on a certain condition
Suffix | Description | Example | Example explanation
S | Update APSR (flags) | ADDS R1, #0x21 | Add 0x21 to R1 and update APSR
EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE | Condition execution e.g. EQ= equal, NE= not equal, LT= less than | BNE label | Branch to the label if not equal

## Slide 40: Data Insertion and Alignment
Insert data inside programs
  DCD: insert a word-size data
  DCB: insert a byte-size data
  ALIGN:
    used before inserting a word-size data
    Uses a number to determine the alignment size
For example
  …
  ALIGN 4 ; Align to a word boundary
  MY_DATA DCD 0x12345678 ; Insert a word-size data
  MY_STRING DCB “Hello”, 0 ; Null terminated string
  …

## Slide 41: Useful Resources
Architecture Reference Manual:
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi0403c/index.html
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf