## Slide 1: The ARM Cortex-M0 Processor Architecture – part1

## Slide 2: Module Syllabus
ARM Architectures and Processors
  What is ARM Architecture
  ARM Processors Families
  ARM Cortex-M Series Family
  Cortex-M0 Processor
  ARM Processor Vs. ARM Architectures
ARM Cortex-M0 Processor
  Cortex-M0 Processor Overview
  Cortex-M0 Block Diagram
  Cortex-M0 Registers
Cortex-M0 Memory Map
Cortex-M0 Exception Handling

## Slide 3: ARM Architectures and ARM Processors

## Slide 4: What is ARM Architecture
ARM architecture is a family of RISC-based processor architectures
  Well-known for its power efficiency;
  Hence widely used in mobile devices, such as smartphones, and tablets
  Designed and licensed to a wide eco-systems by ARM.
ARM Holdings
  The company designs ARM-based processors;
  Does not manufacture, but licenses designs to semiconductor partners who fabricate and sell to their customers;
  Also offer other designs available, such as physical IPs, graphics cores, and development tools.

## Slide 5: ARM Processor Families
Cortex-A series (Application)
  High performance processors for open Operating Systems;
  Applications include smartphones, digital TV, smart books, home gateways;
Cortex-R series (Real-time)
  Exceptional performance for real-time applications;
  Applications include automotive braking systems, powertrains;
Cortex-M series (Microcontroller)
  Cost-sensitive solutions for deterministic microcontroller applications;
  Applications include microcontrollers, mixed signal devices, smart sensors, automotive body electronics and airbags;
SecurCore series
  High security applications.
Previous classic processors
  Include ARM7, ARM9, ARM11 families
Cortex-A
Cortex-A57
Cortex-A53
Cortex-A15
Cortex-A9
Cortex-A8
Cortex-A7
Cortex-A5
Cortex-R7
Cortex-R5
Cortex-R4
Cortex-M4
Cortex-M3
Cortex-M1
Cortex-M0+
Cortex-M0
SC000
SC100
SC300
ARM11
ARM9
ARM7
Cortex-R
Cortex-M
SecurCore
Classic
As of Sept 2013

## Slide 6: Design an ARM-based SoC
Select a set of IP cores from ARM or other third-party IP vendors;
Integrate IP cores into a single chip design;
Give design to semiconductor foundries for chip fabrication.
ARM-based
MCU Chip
ROM
ARM
processor
RAM
System bus
Peripherals
External Interface
SoC
SoC Design
Chip Manufacture
Licensable IPs
IP libraries
Cortex-A9
Cortex-R5
Cortex-M0
ARM7
ARM9
ARM11
AXI bus
AHB bus
APB bus
GPIO
I/O blocks
Timer
DRAM ctrl
FLASH ctrl
SRAM ctrl

## Slide 7: ARM Cortex-M Series Family
Cortex-M series: Cortex-M0, M0+, M1, M3, M4.
Energy-efficiency
  Lower energy costs, longer battery life
Smaller code
  Lower silicon costs
Ease of use
  Faster software development and reuse
Embedded applications
  Smart metering, human interface devices, automotive and industrial control systems, white goods, consumer products and medical instrumentation
As of Sept 2013

## Slide 8: ARM Cortex-M Series Family
Processor | ARM Architecture | Core Architecture | Thumb® | Thumb®-2 | Hardware Multiply | Hardware Divide | Saturated Math | DSP Extensions | Floating Point
Cortex-M0 | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M0+ | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M1 | ARMv6-M | Von Neumann | Most | Subset | 3 or 33 cycle | No | No | No | No
Cortex-M3 | ARMv7-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | No | No
Cortex-M4 | ARMv7E-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | Yes | Optional

## Slide 9: Cortex-M0 Processor
The smallest ARM processor
  Exceptionally small silicon area
  Ultra-low gate count (approx. 12k gates at minimum configuration)
High code density
  Fundamental base of 16-bit Thumb instructions
  Additional powerful 32-bit instructions
Lower power
  16µW/MHz (90LP process, minimal configuration)
Simplicity
  Only 56 instructions
  C friendly
  More deterministic response time
Uses ARMv6-M Architecture

## Slide 10: ARM Processor Vs. ARM Architectures
ARM architecture
  Describes the details of instruction set, programmer’s model, exception model, and memory map;
  Documented in the Architecture Reference Manual;
ARM processor
  Developed using one of the ARM architectures;
  More implementing details, such as timing information and implementation-related information;
  Documented in processor’s Technical Reference Manual.
ARMv4/ V4t Architecture
ARMv5/ v4E Architecture
ARMv6 Architecture
ARMv7
Architecture
ARM v6-M
e.g. Cortex-M0, M1
e.g. ARM7TDMI
e.g. ARM9926EJ-S
e.g. ARM1136
ARMv8 Architecture
ARMv7-A
e.g. Cortex-A9
ARMv7-R
e.g. Cortex-R4
ARMv7-M
e.g. Cortex-M3
ARMv8-A
e.g. Cortex-A53
Cortex-A57
ARMv8-R
As of Sept 2013

## Slide 11: ARM Processor Vs. ARM Architectures
Cortex-M0: v6-M
  ARMv6 architecture’s thumb instruction set;
  ARMv7-M architecture memory map, exception model, and thumb-2 system;
  Low power optimised design.
ARM v6-M
Architecture
ARM v6
Architecture
ARM v7-M
Architecture
ARM
Cortex-M0
Thumb Instruction set
Memory map
Exception Model
Thumb-2 system
Low power optimized
design

## Slide 12: ARM Cortex-M0 Processor Overview

## Slide 13: Cortex-M0 Overview
32-bit Reduced Instruction Set Computing (RISC) processor
Von-Neumann architecture
  Both data and instructions share a single bus interface;
Instruction set
  56 instructions as a subset of Thumb-1 (16-bit) and Thumb-2 (16/ 32-bit);
Supported Interrupts
  Non-maskable Interrupt (NMI) + 1 to 32 physical interrupts
Supports Sleep Modes

## Slide 14: Cortex-M0 Block Diagram
Internal Bus System
AHB LITE
Bus interface
Wakeup
Interrupt
Controller (WIC)
Processor
Core
Nested Vector
Interrupt
Controller
(NVIC)
Debug
Subsystem
Interrupt
Requests and NMI
ARM Cortex-M0 Microprocessor
Memory and peripherals
JTAG/Serial-Wire
Debug Interface
Power management interface

## Slide 15: Cortex-M0 Block Diagram
Processor core
  Contains internal registers, the ALU, data path, and some control logics;
  Three-stage pipeline: fetch, decode, and execution;
  Registers include sixteen 32-bit registers for both general and special usages.
Nested Vectored Interrupt Controller (NVIC)
  Up to 32 interrupt request signals and a non-maskable interrupt (NMI);
  Automatically handles nested interrupts, such as comparing priorities between interrupt requests and the current priority level;
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Instruction 1
Instruction 2
Instruction 3
Fetch
Decode
Execute
Instruction 4
Time

## Slide 16: Cortex-M0 Block Diagram
Bus system
  Includes the internal bus system, the data path in the processor core, and the AHB LITE interface unit;
  All 32 bits wide;
  AHB LITE is an on-chip bus protocol for many ARM processors and widely used in IC design industry.
Debug subsystem
  Handles debug control, program breakpoints, and data watchpoints;
  When a debug event occurs, it can put the processor core in a halted state, where developers can analyse the status of the processor at that point, such as register values and flags.
Wakeup Interrupt Controller (WIC) (optional)
  For low-power applications, the microcontroller can enter sleep mode by shutting down most of the components.
  When an interrupt request is detected, the WIC can inform the power management unit to power up the system.

## Slide 17: ARM Cortex-M0 Processor Registers

## Slide 18: Cortex-M0 Registers
Processor registers
  The internal registers are used to store and process temporary data within the processor core;
  All registers are inside the processor core hence can be accessed more quickly;
  Load-store architecture
          To process a data in the memory, they have to be loaded from the memory to a register, processed inside the processor, and then written back to the memory if needed;
Cortex-M0 register
  Register bank
          Sixteen 32-bit registers (thirteen are used for general-purpose);
  Special registers;

## Slide 19: Cortex-M0 Registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status
Registers (PSR)
Interrupt mask register
Stack definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General purpose
register

## Slide 20: Cortex-M0 Registers
R0 – R12: general purpose registers
  Low registers (R0 – R7) can be accessed by any instruction;
  High registers (R8 – R12) sometimes cannot be accessed by some Thumb instructions;
R13: Stack Pointer (SP)
  Records the current address of the stack
  Used for saving the context of a program while switching between tasks
  Cortex-M0 has two SPs: Main SP, used in applications that require privileged access e.g. OS kernel, and exception handlers, and Process SP, used in base-level application code (when not running an exception handler)
Program Counter (PC)
  Records the address of the current instruction code;
  Automatically incremented by 4 at each operation (for 32-bit instruction code), except branching operations;
  A branching operation, such as function calls, will change the PC to a specific address, meanwhile save the current PC to the Link Register (LR);
Data
Data
PC
SP
Address
Low
High
PUSH
POP
Stack
Code
Heap

## Slide 21: Cortex-M0 Registers
R14: Link Register (LR)
  The LR is used to store the return address of a subroutine or a function call;
  The program counter (PC) will load the value from LR after a function is finished;
PC
LR
Main
Program
code
subroutine
Current PC
Load PC with the address in LR to return to the main program
Current LR
Return from a subroutine to the main program
PC
LR
Main
Program
code
subroutine
Current PC
1. Save current
PC to LR
2. Load PC with the starting address of the subroutine
Call a subroutine
Code region
Code region

## Slide 22: Cortex-M0 Registers
xPSR, combined Program Status Register
  Provides the information about program execution and the ALU flags;
    Application PSR (APSR)
    Interrupt PSR (IPSR)
    Execution PSR (EPSR)
N
Z
C
V
ISR number
Reserved
Reserved
Reserved
T
Reserved
T
N
Z
C
V
ISR number
APSR
IPSR
EPSR
xPSR
bit0
bit8
bit16
bit24
bit31

## Slide 23: Cortex-M0 Registers
APSR
  N: negative flag
          Set to one if the result from ALU is negative;
  Z: zero flag
          Set to one if the result from ALU is zero;
  C: carry flag
          Set to one if an unsigned overflow occurs;
  V: overflow flag
          Set to one if a signed overflow occurs;
IPSR
  ISR number
          Current executing interrupt service routine number
EPSR
  T: Thumb state
          Always one since Cortex-M0 only supports the Thumb state

## Slide 24: Cortex-M0 Registers
PRIMASK: Interrupt Mask Special Register
  1-bit PRIMASK
          Set to one will block all the interrupts apart from nonmaskable interrupt (NMI) and the hard fault exception;
CONTROL: special register
  1-bit stack definition
          Set to one: use the process stack pointer (PSP);
          Clear to zero: use the main stack pointer (MSP).
Reserved
Reserved
PRIMASK
PRIMASK
CONTROL
bit8
bit16
bit24
bit31
Stack definition

## Slide 25: ARM Cortex-M0 Processor Memory Map

## Slide 26: Cortex-M0 Memory Map
The Cortex-M0 processor has 4 GB of memory address space
The 4GB memory space is architecturally defined as a number of regions.
  Each region is given for recommended usage;
  Easy for software programmer to port between different devices.
Nevertheless, despite of the default memory map, the actual usage of the memory map can also be flexibly defined by the user, except some fixed memory addresses, such as internal private peripheral bus.

## Slide 27: Cortex-M0 Memory Map
Private peripherals
e.g. NVIC, SCS
Mainly used for external peripherals
e.g. SD card
Mainly used for external memories
e.g. external DDR, FLASH, LCD
Mainly used for on-chip peripherals
e.g. AHB, APB peripherals
Mainly used for data memory
e.g. on-chip SRAM, SDRAM
Mainly used for program code
e.g. on-chip FLASH
Reserved
External Device
External RAM
Peripherals
SRAM
Code
0xFFFFFFFF
0xE0000000
Private Peripheral Bus
0xDFFFFFFF
0xA0000000
0x9FFFFFFF
0x60000000
0x5FFFFFFF
0x40000000
0x3FFFFFFF
0x1FFFFFFF
0x20000000
0x00000000
512MB
512MB
512MB
1GB
1GB
512MB
0xE00FFFFF
0xE0100000
Reserved for other purposes
ROM table
Reserved
System Control Space
(SCS)
Reserved
Break point unit
Data watch point unit
Reserved
Debug Control
Nested Vectored
Interrupt Controller
(NVIC)
Reserved
SysTick Timer
Reserved
System Control Block
(SCB)

## Slide 28: Cortex-M0 Memory Map
Code Region
  Primarily used to store program code;
  Can also be used for data memory;
  On-chip memory, such as on-chip FLASH.
SRAM Region
  Primarily used to store data, such as heaps and stacks;
  Can also be used for program code;
  On-chip memory; despite its name “SRAM”, the actual device could be SRAM, SDRAM or other types.
Peripheral Region
  Primarily used for peripherals, such as Advanced High-performance Bus (AHB) or Advanced Peripheral Bus (APB) peripherals;
  On-chip peripherals.

## Slide 29: Cortex-M0 Memory Map
External RAM Region
  Primarily used to store large data blocks, or memory caches;
  Off-chip memory, slower than on-chip SRAM region.
External Device Region
  Primarily used to map to external devices;
  Off-chip devices, such as SD card.
Internal Private Peripheral Bus (PPB)
  Used inside the processor for processor’s internal control;
  Within PPB, a special range of memory is defined as System Control Space (SCS);
  Nested Vectored Interrupt Controller (NVIC) is part of SCS.

## Slide 30: Cortex-M0 Memory Map Example
AHB bus
External SRAM,
FLASH
External LCD
SD card
Cortex-M0
PPB
SCS
NVIC
Debug Ctrl
On-chip FLASH
(Code Region)
On-chip SRAM
(SRAM Region)
Peripheral Region
External memory interface
(External RAM Region)
External device interface
(External Device Region)
Timer
UART
GPIO
Chip Silicon

## Slide 31: Cortex-M0 Program Image
The program image in Cortex-M0 contains
  Vector table -- includes the starting addresses of exceptions (vectors) and the value of the main stack point (MSP);
  C start-up routine;
  Program code – application code and data;
  C library code – program codes for C library functions.
0x00000000
Initial MSP value
Code region
Start-up routine &
Program code &
C library code
Vector table
Program
Image
Reset vector
NMI vector
Hard fault vector
Reserved
SVC vector
Reserved
PendSV vector
SysTick vector
Interrupt vectors
0x00000000
0x00000004
0x00000008
0x0000000C
0x0000002C
0x00000038
0x00000040
0x0000003C

## Slide 32: Cortex-M0 Program Image
After reset:
  First reads the initial MSP value;
  Then reads the reset vector;
  Branches to the starting of the programme execution address (reset handler);
  Subsequently executes program instructions.
Reset
Fetch initial value for MSP
(Read address 0x00000000)
Fetch reset vector
(Read address 0x00000004)
Fetch 1st instruction
(Read address of reset vector)
Fetch 2nd instruction
(Read subsequent instructions)

## Slide 33: Cortex-M0 Endianness
Endian refers to the order of bytes stored in the memory
  Little endian: lowest byte of a word-size data is stored in the bit 0 to bit 7
  Big endian: lowest byte of a word-size data is stored in the bit 24 to bit 31
Cortex-M0 supports both little endian and big endian
However, Endianness only exists in the hardware level
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
0x00000000
0x00000004
0x00000008
Address
[7:0]
[15:8]
[23:16]
[31:24]
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
Byte0
Byte1
Byte2
Byte3
[7:0]
[15:8]
[23:16]
[31:24]
Word 1
Word 2
Word 3
Word 1
Word 2
Word 3
Little endian 32-bit memory
Big endian 32-bit memory

## Slide 34: ARM Cortex-M0 Processor Exceptions

## Slide 35: Cortex-M0 Exception Handling
Exceptions are events that cause the program flow to exit the current program thread, and execute a piece of code associated with the event.
Events can be either internal or external.
The external event is also called interrupt request (IRQ).
Thread
Mode
Exception
Mode
Internal or external event
Executing exception
handler
Executing normal code sequence
Finishing handler
Context saving
Context restoring

## Slide 36: Cortex-M0 Exception Handling
Exception Handler
  A piece of software code that is executed in the exception mode;
  If the exception is caused by an IRQ, it can also be called as an interrupt handler, or interrupt service routine (ISR);
Context Switching
  Context saving: before entering the exception mode, the current program context, such as current registers values, are pushed onto the stack;
  Context restoring: after finishing the handler, the previously stored context is restored by popping register values from the stack.
Thread
Mode
Exception
Mode
Internal or external event
Executing exception
handler
Executing normal code sequence
Finishing handler
Context saving
Context restoring

## Slide 37: Cortex-M0 Exception Handling
Exception Priority
  The exceptions (or interrupts) are commonly divided into multiple levels of priorities;
  A higher priority exception can be triggered and serviced during a lower priority exception;
  Commonly known as a nested exception.
  Exceptions can be disabled or enabled by software.
Cortex-M0 Interrupt Controller
  Supports up to 32 IRQ inputs and a non-maskable interrupt (NMI) inputs;
  NMI is similar to IRQ but cannot be disabled and has the highest priority, useful for safety critical systems such as industrial control or automotive.

## Slide 38: Vector Table for ARMv6-M
First entry contains initial Main SP
All other entries are addresses for exception handlers
  Must always have LSBit = 1 (for Thumb)
Table has up to 496 external interrupts
  Implementation-defined
  Maximum table size is 2048 bytes
Table may be relocated
  Use Vector Table Offset Register
  Still require minimal table entries at 0x0 for booting the core
Each exception has a vector number
  Used in Interrupt Control and State Register to indicate the active or pending exception type
Table can be generated using C code
  Example provided later
Reserved (x4)
Usage Fault
Mem Manage Fault
Hard Fault
NMI
Reset
Initial Main SP
0x1C to 0x28
0x18
0x14
0x10
0x0C
0x08
0x04
0x00
16 + N
…
16
15
14
13
12
11
SVC
Debug Monitor
Reserved
PendSV
SysTick
External 0
Bus Fault
…
External N
0x40 + 4*N
…
0x40
0x3C
0x38
0x34
0x30
0x2C
7-10
6
5
4
3
2
1
N/A
Address
Vector #

## Slide 39: Vector Table in Assembly
The interrupt vector can be defined in either C language or assembly language, for example in assembly:
RESERVE8
THUMB
IMPORT ||Image$$ARM_LIB_STACK$$ZI$$Limit||
AREA RESET, DATA, READONLY
EXPORT __Vectors
__Vectors DCD ||Image$$ARM_LIB_STACK$$ZI$$Limit|| ; Top of Stack
DCD Reset_Handler ; Reset Handler
DCD NMI_Handler ; NMI Handler
DCD HardFault_Handler ; Hard Fault Handler
DCD MemManage_Handler ; MemManage Fault Handler
DCD BusFault_Handler ; Bus Fault Handler
DCD UsageFault_Handler ; Usage Fault Handler
DCD 0, 0, 0, 0, ; Reserved x4
DCD SVC_Handler, ; SVCall Handler
DCD Debug_Monitor ; Debug Monitor Handler
DCD 0 ; Reserved
DCD PendSV_Handler ; PendSV Handler
DCD SysTick_Handler ; SysTick Handler
; External vectors start here

## Slide 40: Useful Resources
Reference1
  Book: “The Definitive Guide to the ARM Cortex-M0” by Joseph Yiu, ISBN-10: 0123854776, ISBN-13: 978-0123854773, March 11, 2011
Reference2
  ARM v6-M Architecture Reference Manual:
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi041 9c/index.html
Reference3
  Cortex-M0 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0432c/DDI0432 C_cortex_m0_r0p0_trm.pdf